## Slide 1: Resolving the Scell dropping using power limits on serving cells for FR1 and FR2
Attachment to R4-2118129
Ericsson
3GPP TSG-RAN WG4 Meeting #101-e
Electronic meeting, 1 – 12 November 2021
R4-2118129

## Slide 2: Background
For any CA band combination, the UE configures
  a configured maximum output power PCMAX,f,c for each serving cell c of the configuration
  a configured maximum output power PCMAX for the total power of the configuration
When the PCMAX is exceeded, the UE prioritizes the transmissions according to the rules in clause 7.5 of 38.213
Configure in RRC relative UE-specific limits on DPCMAX,f,c on PCMAX,f,c on one or more of the serving cells c in the uplink configuration
These limits can be enabled/disabled by MAC-CE for fast adaptation
The limits apply for concurrent UL transmissions
  if only high priority transmission scheduled this would get all available power up to PCMAX

## Slide 3: No limits: dropping or scaling Scells
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
Ppower class
Reduced or dropped
PCMAX,f,c
PPUSCH,f,PCell
PPUSCH,f,SCell
The intra-band case shown above, the actual power back-off is not known to the gNB and for FR2 the plane of reference of – and hence also the absolute reference level of – PCMAX is not known

## Slide 4: Limit on Pcell and the Scell scaled
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,PCell
PPUSCH,f,PCell = PCMAX,f,Pcell (reduced)
Ppower class
PPUSCH,f,SCell
PCMAX,f,SCell
The UE may still drop the Scell (no restriction in 38.213) instead of scaling

## Slide 5: Limit on both cells, dropping will not occur
PCell
PUSCH
Scell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,Pcell = DPCMAX,f,Scell = 3 dB
Ppower class
The actual UE back-off can be any value, both cells are still 3 dB below, works for both FR1 and FR2

## Slide 6: If only one cell scheduled, limits do not apply
PCell
PUSCH
BW
BW
f
PCMAX
Total power back-off ≤ MPR
UE output power (PSD)
DPCMAX,f,Pcell = DPCMAX,f,Scell = 3 dB
Ppower class
No other transmission overlapping a slot of a scheduled transmission
Reduces the need for enabling/disabling limits by MAC-CE signaling

## Slide 7: Summary
The solution feasible for both FR1 and (at least for intra-band) for FR2
RAN1 impact to be confirmed, but only PCMAX,f,c per cell is affected
  The priority mechanism in 38.213 not affected as such, the UE power per cell is limited by PCMAX,f,c regardless of priority of transmission
Solves the ”equal PSD” issue in RAN5
...and can also be used in the field