## Slide 1: WF on NS_21 Regulatory Requirements
Qualcomm Inc., [Apple], …
R4-2119840
3GPP TSG-RAN WG4 Meeting #101-e
Electronic meeting, 1st – 12th November 2021

## Slide 2: Background and Problem:
Introduction to n30 by supporting US operators proposed in [6]
AMPR and NS_21 originally introduced in [7] based on US regulatory FCC 27.53 requirements
WF in last meeting required AMPR modification in n30 due to Canadian regulatory requirements [4].
Operation in Canada requires Canadian RSS-195 requirements which are tighter than FCC 27.53 in 1MHz band outside channel BW and see next slide [1].
  Need to clarify why the intention of RSS-195 does not follow FCC.
Cannot modify NS_21 for RSS-195 as this Canadian regulatory requirement is not required for US operation.
UEs in US should not be subjected to unnecessary back-off that would degrade link performance by NS_21 modification.
Newly introduced UEs operating in WCS2300MHz band in Canada are subjected to extra back-off according to RSS-195 and as shown in [2] [3] [5].

## Slide 3: Background (RSS-195 Vs FCC bullet point 3 previous slide):
The FCC document states that a narrower resolution bandwidth (RBW) is permissible if RBW is >= 1% of the channel BW. So, the specification can be -13dBm/ (1% channel BW) for 0-1MHz from channel edge. Only if RBW < 1% of channel BW, the power is integrated over 1MHz.
RSS-195 states that RBW must be >= 1% of the channel BW (cannot be < 1%) and power must be integrated over 1MHz, so the specification is -13dBm/1MHz for 0-1MHz from the channel edge.
5MHz Channel BW
0 MHz
-1 MHz
-6 MHz
-10 MHz
-13dBm/MHz
-25dBm/MHz
-13dBm/50KHz
-13dBm/MHz
WCS in FCC Section 27.53
WCS in RSS-195

## Slide 4: WF (Overall):
Other North American Bands shared between US and Canada do not have strict adjacent 0-1 MHz requirements as in RSS-195, so why should WCS2300MHz be any different?
  Send LS to Canada regulatory to find out why RSS-195 does not follow FCC 27.53 or find out the intention of the strict requirement.
  Introduce LS in RAN4#101Bis
Due to response of time of LS, introduce new NS value (NS_XX) for n30 in Table 6.2.3.1-1 (slide 5) to prevent unwanted backoff in US WCS2300 band.
  Add Value of Added Spectrum Emission = 2 for n30 in Table 6.2.3.1-1A to indicate NS_XX for Canada region only (slide 5)
  Introduce added ASEM requirement for new NS_XX as proposed in [4] but for only 5MHz and 10MHz channel BWs (slide 6).
  Use AMPR values in [2][3][5] for NS_XX for 5MHz channel BW and apply 10MHz AMPR values in NS_21 for NS_XX 10MHz channel BW (slide 7).

## Slide 5: WF (NS Value Introduction):
Introduce new NS value (NS_XX) for n30 in Table 6.2.3.1-1.
Add Value of Added Spectrum Emission = 2 for n30 in Table 6.2.3.1-1A to indicate NS_XX for Canada region only.
Table 6.2.3.1-1: Additional maximum power reduction (A-MPR)
Table 6.2.3.1-1A: Mapping of network signalling label
Network signalling label | Requirements (clause) | NR Band | Channel bandwidth (MHz) | Resources blocks (NRB) | A-MPR (dB)
NS_XX | 6.5.3.3.12 6.5.2.3.5 | n30 | 5, 10 |  | Clause 6.2.3.ZZ
NR band | Value of additionalSpectrumEmission |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
n30 | NS_01 | NS_21 | NS_XX |  |  |  |  | 

## Slide 6: WF (AMPR Requirements):
Introduce ASEM requirements for NS_XX in clause 6.5.2.3 as proposed in [4] but for only 5MHz and 10MHz channel BWs
Apply ASPUR requirements in clause 6.5.3.3.12 for NS_21 and NS_XX.
Table 6.5.2.3.5-1: Additional requirements for "NS_XX"
ΔfOOB MHz | Channel bandwidth (MHz) / Spectrum emission limit (dBm) |  | Measurement bandwidth
 | 5 | 10 | 
 0-1 | -13 | -13 | 1 MHz
 1-6 | -13 | -13 | 1 MHz
 6-10 | -25 | -13 | 1 MHz
 10-15 |  | -25 | 1 MHz
Table 6.5.3.3.12-1: Additional requirements for "NS_21 and NS_XX"
Frequency band (MHz) | Channel bandwidth (MHz) / Spectrum emission limit (dBm) | Measurement bandwidth
 | 5, 10 | 
2200 ≤ f < 2288 | -40 | 1 MHz
2288 ≤ f < 2292 | -37 | 1 MHz
2292 ≤ f < 2296 | -31 | 1 MHz
2296 ≤ f < 2300 | -25 | 1 MHz
2320 ≤ f < 2324 | -25 | 1 MHz
2324 ≤ f < 2328 | -31 | 1 MHz
2328 ≤ f < 2332 | -37 | 1 MHz
2332 ≤ f ≤ 2395 | -40 | 1 MHz

## Slide 7: WF (AMPR):
Introduce new AMPR values for 5MHz channel BW as proposed in [2] [3] [5] for NS_XX.
Keep same 10MHz AMPR values as in NS_21 for 10MHz NS_XX
Channel Bandwidth (MHz) | Modulation/Waveform |  | Region A1a RBstart ≤ 0.36MHz/12/SCS LCRB ≤ [0.54] MHz/12/SCS | Region A1b RBstart ≤ 0.36MHz/12/SCS LCRB > [0.54] MHz/12/SCS LCRB ≤ 2.52MHz/12/SCS | Region A2 LCRB > 2.52MHz/12/SCS | Region A3b RBend ≥ 3.96MHz/12/SCS LCRB > [0.54] MHz/12/SCS LCRB ≤ 2.52MHz/12/SCS | Region A3a RBend ≥ 3.96MHz/12/SCS LCRB ≤ [0.54] MHz/12/SCS
 |  |  | Outer/Inner |  | Outer | Outer/Inner | 
5 | DFT-s-OFDM | PI/2 BPSK | ≤ 4.0 | ≤ 2.0 | ≤ 1.5 | 2.0 | 4.0
 |  | QPSK | ≤ 4.5 | ≤ 2.5 | ≤ 2.0 | ≤ 2.5 | ≤ 4.5
 |  | 16 QAM | ≤ 4.5 | ≤ 2.5 | ≤ 2.5 | ≤ 2.5 | ≤ 4.5
 |  | 64 QAM | ≤ 4.5 | ≤ 2.5 | ≤ 2.5 | ≤ 2.5 | ≤ 4.5
 |  | 256 QAM | ≤ 4.5 | ≤ 4.5 | ≤ 4.5 | ≤ 4.5 | ≤ 4.5
 | CP-OFDM | QPSK | ≤ 4.5 | ≤ 4.0 | ≤ 4.0 | ≤ 4.0 | ≤ 4.5
 |  | 16 QAM | ≤ 4.5 | ≤ 4.0 | ≤ 4.0 | ≤ 4.0 | ≤ 4.5
 |  | 64 QAM | ≤ 4.5 | ≤ 4.0 | ≤ 4.0 | ≤ 4.0 | ≤ 4.5
 |  | 256 QAM | ≤ 6.5 | ≤ 6.5 | ≤ 6.5 | ≤ 6.5 | ≤ 6.5
Channel Bandwidth (MHz) | Modulation/Waveform |  | Region A1a RBstart ≤ 1.44MHz/12/SCS LCRB ≤ [0.54] MHz/12/SCS | Region A1b RBstart ≤ 1.44MHz/12/SCS LCRB > [0.54] MHz/12/SCS LCRB ≤ 2.16MHz/12/SCS | Region A2 LCRB > 5.4MHz/12/SCS | Region A3b RBend ≥ 7.74MHz/12/SCS LCRB > [0.54] MHz/12/SCS LCRB ≤ 2.16MHz/12/SCS | Region A3a RBend ≥ 7.74MHz/12/SCS LCRB ≤ [0.54] MHz/12/SCS
 |  |  | Outer/Inner |  | Outer | Outer/Inner | 
10 | DFT-s-OFDM | PI/2 BPSK | 6 | 3 | 4 | 3 | 6
 |  | QPSK | 6 | 3 | 4 | 3 | 6
 |  | 16 QAM | 6 | 3 | 4 | 3 | 6
 |  | 64 QAM | 6 | 3 | 4 | 3 | 6
 |  | 256 QAM | 6 | 3 | 4 | 3 | 6
 | CP-OFDM | QPSK | 6 | 4 | 5.5 | 4 | 6
 |  | 16 QAM | 6 | 4 | 5.5 | 4 | 6
 |  | 64 QAM | 6 | 4 | 5.5 | 4 | 6
 |  | 256 QAM | 6 | 4 | 5.5 | 4 | 6
Table 6.2.3.ZZ-1: A-MPR for "NS_XX"

## Slide 8: References:
[1] R4-2117512 “n30 NS_21 Regulatory Requirement”, Qualcomm Incorporated, RAN4#101-e
[2] R4-2117960 “Follow up on additional requirements and A-MPR for NS_21”, Apple, RAN4#101-e
[3] R4-2117961 “draftCR: Rel-16 Additional requirements and A-MPR for NS_21 and n30”, Apple, RAN4#101-e
[4] R4-2115084 “WF on NS_21 SEM and A-MPR”, Apple, RAN4#100-e
[5] R4-2112348 “Additional requirements and A-MPR for NS_21 and n30”, Apple, RAN4#100-e
[6] RP-190166 “New WID on introduction of n30”, Ericsson, AT&T, RAN#83, Shenzhen, China
[7] R4-1904649 “n30 NS_21”, Qualcomm Incorporated, RAN4#90Bis, Xi’an, China