## Slide 1: WF on NR FDD PC2 HPUE
Moderator (China Unicom)
3GPP TSG-RAN WG4 Meeting #101-e
Electronic Meeting, November 1st – 12th, 2021
R4-2119946

## Slide 2: Release Independence
Agreement:
  NR FDD PC2 HPUE is release independent from Rel-15.

## Slide 3: UE Tx power and tolerance
Agreement:
  For both 1Tx and 2Tx, UE Tx power: 26dBm; Tolerance: +2/-3dB.

## Slide 4: MPR
Agreement
  MPR for PC2 single Tx and dual Tx apply to FDD bands also.
  PC2 FDD MPR requirements for 2Tx architecture can reuse the MPR requirements of PC2 TxD (2x23dBm) UE.

## Slide 5: A-MPR
Agreement:
  The A-MPR requirements for NS_100, NS_05, NS_05U, NS_48 and NS_49 shall be evaluated for PC2 n1, and NS_100 shall be evaluated for PC2 n3. For NS_48 and NS_49, evaluate A-MPR for BW<=20MHz for power class 2. Update the network signals to include smaller channel bandwidths if found necessary.
  Assumptions for 1Tx A-MPR evaluation:
CIM3: 60 dBc.
CIM5: 70dBc
Focus evaluations first on QPSK DFT-s-OFDM with Image and carrier leakage of 28dB for up to 64QAM.
Evaluation of Higher order modulations is not precluded, for 256QAM image is 35dB,
PA calibration for 20 MHz, SCS 15 kHz, QPSK, DFT-S-OFDM, 100 RB0 waveform to meet 31dB ACLR at 1 dB MPR based on [4~5]dB post PA losses,
Post PA insertion loss: [4~5] dB
PC2 studies assume the same filter rejection than those used for PC3 studies

## Slide 6: A-MPR (continued)
    Assumptions for 2Tx A-MPR evaluation:
  To recreate the effect of CDD the two signals on each antenna can simply have a small delay between each other,
  Focus evaluations first on DFT-s-OFDM QPSK waveforms,
  Evaluation of Higher order modulations is not precluded,
  Since simulation may not be available, at least some worst case corners are evaluated for inner/outer and edge allocations.
RF assumptions:
- PC2 with 2x23dBm PAs
- [4~5]dB post PA losses
- 10dB antenna isolation
- Equal power and Equal back-off power split for the two antennas
- Image and carrier leakage is 28dB for up to 64QAM, image is 35dB for 256QAM
- CIM3 is 60dB and CIM5 is 70dB
- PC2 studies assume the same filter rejection than those used for PC3 studies
PA calibration for 20MHz SCS15kHz QPSK DFT-s-OFDM 100RB0 waveform based on [4~5]dB post PA losses to meet 30dB ACLR at 1dB MPR

## Slide 7: ACLR
Agreement:
  PC2 ACLR of 31 dB applies. General emission requirements apply unchanged for PC2. Emission requirements apply to the power sum of antenna ports for a 2Tx architecture. Existing UTRA ACLR requirement applies for PC3 and PC2 when NS_100 or NS_xxU is signalled.

## Slide 8: MSD requirements
Agreement:
  Companies need more time to check MSD requirements for n1 and n3 PC2 under 1Tx and 2Tx architecture.
  PC2 MSD:
    Option 1: Use PC3 REFSENS requirements as reference point, FFS if “MSD” is appropriate to capture PC2 REFSENS level, e.g. use DeltaPC2_REFSENS instead of PC2 MSD.
    Option 2: Define PC2 MSD using ideal RB scaled REFSENS level as reference point.

## Slide 9: Way Forward
Companies are encouraged to provide further analyses in next meeting based on the agreements.