## Slide 1: Motivation on basket WID on 4Rx support for NR FR1 bands in Rel-18
3GPP TSG-RAN WG4 Meeting #104-e R4-2212737
Electronic Meeting, Aug. 15-Aug. 26, 2022
Source: ZTE Corporation
Agenda Item: 15

## Slide 2: Backgroud
The 4Rx requirements have been introduced for some FR1 bands for different form factors in the past. The purpose by introducing the 4Rx support for some bands is to provide higher throughput and better coverage.
A new WID [1] on 4Rx support for NR band n8 was approved, with the same consideration of 600MHz (n71) and 700MHz band (n28), i.e. 4 Rx operation is targeted for FWA form factor.
Currently, there were several NR bands already supported 4Rx. However, there were some other bands smaller than 2.6GHz not supporting 4Rx
Reference:
[1] RP-213659, New WID: 4Rx support for NR band n8, CHTTL
[2] RP-220987, New WID on Further RF requirements enhancement for NR frequency range 1 (FR1), Huawei

## Slide 3: 4Rx
More bands may be requested by operators to support 4Rx in Rel-18, by using the current approach, individual WIDs will be needed for different bands, which is not an efficient way for RAN4 WIDs management. Therefore, it is proposed to create a basket WID to include all possible bands requested by operators to support 4Rx in Rel-18.
RF aspect:
  REFSEN requirements: only ΔRIB,4R value should be defined for the bands supporting 4Rx with the specific form factor
Performance aspect:
  Release independence in TS38.307 is needed to be updated if any.

## Slide 4: Proposal
Create a basket WID to include the possible bands (<2.6GHz) requested by operators to support both 4Rx and 8Rx in Rel-18.

## Slide 5: Thank you