## Slide 1: WF for repeater conformance test
R4-2220225
Ericsson

## Slide 2: WF for spectrum purity requirement
The spectrum purity requirement shall be expressed as relative values
The following requirements shall be used as a reference for spectrum purity requirements: ACLR and OBUE

## Slide 3: Spectrum purity requirement for FR1
Center frequency of measurement filter | Minimum requirements | Measurement filter type and filter bandwidth | Integration bandwidth
50.0 kHz outside from channel edge | 46.8 dBc (Note 1) | Square (100 kHz) | 100 kHz
Center of adjacent channel frequency with same nominal channel BW | 46.8 dBc (Note 2) | Square (nominal channel BW) | Nominal channel BW
NOTE 1: the reference spectral density shall be taken at the carrier center frequency with an integration bandwidth of 100 kHz. NOTE 2: the reference spectral densigy shall be taken at the carrier center frequency with an integration bandwidth of nominal carrier BW |  |  | 

## Slide 4: Spectrum Purity Requirement for FR2 (24.25-33.4 GHz)
Center frequency of measurement filter | Minimum requirements | Measurement filter type and filter bandwidth | Integration bandwidth
0.5 MHz outside from channel edge | 28.7 dBc (Note 1) | Square (1 MHz) | 1 MHz
Center of adjacent channel frequency with same nominal channel BW | 28.7 dBc (Note 2) | Square (nominal channel BW) | Nominal channel BW
NOTE 1: the reference spectral density shall be taken at the carrier center frequency with an integration bandwidth of 1 MHz. NOTE 2: the reference spectral densigy shall be taken at the carrier center frequency with an integration bandwidth of nominal carrier BW |  |  | 

## Slide 5: Spectrum Purity Requirement for FR2 (37-43.5 GHz)
Center frequency of measurement filter | Minimum requirements | Measurement filter type and filter bandwidth | Integration bandwidth
0.5 MHz outside from channel edge | 26.4 dBc (Note 1) | Square (1 MHz) | 1 MHz
Center of adjacent channel frequency with same nominal channel BW | 26.4 dBc (Note 2) | Square (nominal channel BW) | Nominal channel BW
NOTE 1: the reference spectral density shall be taken at the carrier center frequency with an integration bandwidth of 1 MHz.. NOTE 2: the reference spectral densigy shall be taken at the carrier center frequency with an integration bandwidth of nominal carrier BW |  |  | 

## Slide 6: Spectrum Purity Requirement for FR2 (43.5-48.2 GHz)
Center frequency of measurement filter | Minimum requirements | Measurement filter type and filter bandwidth | Integration bandwidth
0.5 MHz outside from channel edge | 26.2 dBc (Note 1) | Square (1 MHz) | 1 MHz
Center of adjacent channel frequency with same nominal channel BW | 26.2 dBc (Note 2) | Square (nominal channel BW) | Nominal channel BW
NOTE 1: the reference spectral density shall be taken at the carrier center frequency with an integration bandwidth of 1 MHz. NOTE 2: the reference spectral densigy shall be taken at the carrier center frequency with an integration bandwidth of nominal carrier BW |  |  | 

## Slide 7: WF for spectrum purity requirements
Testability for FR2 requirements:
  No testability constraints captured in the specification