## Slide 1: UE Specific Channel Bandwidths and alignment with the 100 kHz raster
T-Mobile USA, TELUS
3GPP TSG-RAN4 Meeting #107 R4-2309711
Incheon, Korea (Republic Of), 22nd May 2023 - 26th May 2023

## Slide 2: Overview
Background
Signalling of BWPs and UE specific channel BWs
Issues with requiring BWPs and UE specific channel BWs to be centered on the 100 kHz raster
Summary
Status in RAN4

## Slide 3: Background
LTE used a 100 kHz raster (or technically ΔFRaster) for aligning the center frequencies of channels
NR uses a 5 kHz global raster below 3 GHz, and a 15 kHz global raster above 3 GHz.
Other than n41, FR1 bands below 3 GHz (mostly LTE refarmed bands) use the 100 kHz raster, while other (primarily greenfield) bands use the SCS based raster (15 or 30 kHz)
1930 MHz
1950 MHz
Fc=1940 MHz
https://www.nrexplained.com/raster

## Slide 4: Background (continued)
Prior to the introduction of a UE specific channel BW, there was only a cell specific channel bandwidth. The cell specific channel bandwidth broadcast in SIB1 was centered on the 100 kHz raster for bands that use the 100 kHz raster. (This ppt is only dealing with bands that use the 100 kHz raster, and “centered” is of course referring to the position of the appropriate subcarrier closest to the center)
When UE specific channel BWs were introduced at RAN#82 [RP-182482, RP-182896] there was no mention of UE specific channel BWs needing to be centered on the 100 kHz raster.
In the Irregular Channel Bandwidth Study Item discussions in RAN4 there was a revelation that some companies interpreted the specs to require UE specific channel bandwidths to be centered on the 100 kHz raster. This was news to many in RAN4. We (T-Mobile) could not find a requirements documented that UE specific channel bandwidths need to be centered on the 100 kHz raster. Others claimed it is obvious.

## Slide 5: Bandwidth Part location
There is agreement in RAN4 that Bandwidth Parts can be located in any PRBs of the cell specific channel BW n SIB1
In an LS from RAN4 to RAN1 in R4-1811905 "To support forward compatibility, the UE could access the system in such bandwidth(which can be configured anywhere within the gNB channel bandwidth) and would be further configured with a dedicated channel bandwidth based on its capabilities.“
If the UE supports the Cell Specific channel BW, the RF requirements of the Cell Specific channel bandwidth apply
Cell specific channel Bandwidth (30 MHz carrier)
20 MHz UE Specific channel BW
PRB0
PRB1
…
…
…
…
,,,
PRB158
PRB159
…
…
…
Fc= 2125 MHz
PRB1
…
PRB105
…
PRB106
Fc= 2120.32 MHz
PRB0
…
PRB104
…
PRB105
Fc= 2120.14 MHz
PRB2
…
PRB106
…
PRB107
Fc= 2120.5 MHz
…
…
…
…
…
…

## Slide 6: UE Specific channel bandwidth
To be forward compatible, the UE does not need to support the cell specific channel bandwidth in SIB1
In order to make the RF requirements clear, UE specific channel bandwidths were introduced via Qualcomm company CR at RAN#88 in December 2018 in RP-182896
In the discussion on UE specific channel bandwidths, no mention was made of them having to be on the 100 kHz raster, but suddenly allowed BWP positions are not allowed UE specific channel BW positions?
Cell specific channel Bandwidth (30 MHz carrier)
20 MHz UE Specific channel BW
PRB0
PRB1
…
…
…
…
,,,
PRB158
PRB159
…
…
…
Fc= 2125 MHz
PRB1
…
PRB105
…
PRB106
Fc= 2120.32 MHz – not on the 100 kHz raster
PRB0
…
PRB104
…
PRB105
Fc= 2120.14 MHz – not on the 100 kHz raster
PRB2
…
PRB106
…
PRB107
Fc= 2120.5 MHz – on the 100 kHz raster
…
…
…
…
…
…

## Slide 7: Alignment between LTE and NR PRBs
The 100 kHz raster for NR was chosen to be consistent with LTE so that the LTE and NR PRBs align for Dynamic Spectrum Sharing (DSS) between LTE and NR (for the 15 kHz SCS, one PRB = 12 subcarriers * 15 kHz = 180 kHz)
Both BWPs and UE specific channel BWs are defined by offsetToCarrier (integer number of PRBs from PRB 0 of the cell specific channel), the subcarrierSpacing and carrierBandwidth (integer number of PRBs)
Given the Cell Specific channel configuration broadcast in SIB1 is aligned with the 100 kHz channel raster, and the PRBs of the BWP or cell specific channel BWs will align with the PRBs of the cell specific channel BW, the PRBs of BWPs or UE specific carrier bandwidths will also be aligned with the LTE PRBs regardless of whether or not the center frequency of the BWPs or UE specific channel BWs are aligned with the 100 kHz raster
Cell specific channel Bandwidth (10 MHz carrier) Fc= 1940 MHz
10 MHz BWP Fc= 1935.32 MHz
PRB0
PRB1
…
…
…
…
,,,
PRB50
PRB51
…
…
…
PRB1
…
PRB24
…
PRB25
LTE (10 MHz carrier) Fc= 1940 MHz
PRB0
…
…
…
…
,,,
PRB49
…
…
…

## Slide 8: Issues with requiring UE specific channel BWs to be centered on the 100 kHz raster
Issue 1: If the UE specific channel bandwidth center frequencies must be located on the 100 kHz raster, the center frequencies can only be offset from the cell specific channel BW center frequency by an integer multiple of 900 kHz for 15 kHz SCS (LCM of 100 kHz and 180 kHz) or 1.8 MHz for 30 kHz SCS so that the PRBs align. In many cases this would prevent UEs from using intra-band CA to access the full BW.
Issue 2: The cell specific BW broadcast in SIB1 and the UE specific BW must both have even or odd numbers of PRBs if both are required to be centered on the 100 kHz raster. If one is even and one is odd, the PRBs can never align if both center frequencies must be on the 100 kHz raster
  There is no solution to 90+M×180=N×100 where M and N are integers
  This problem proves that the 100 kHz raster restriction for UE specific channel BWs was not thoroughly thought through
Issue 3: Requiring cell specific channel BWs to be on the 100 kHz raster would result in PRB fragmentation for many configurations

## Slide 9: Issue 1: intra-band CA with Legacy channel BWs impossible for many new channel bandwidths
From Qualcomm contribution R4-1810562, “gNBs will have to handle UEs that support the largest gNB configurable CHBW with CA such that legacy UEs can operate their entire aggregated bandwidth despite having limited CHBW”
If the legacy carriers need to be centered on the 100 kHz raster, then in many cases UEs cannot operate in the entire aggregated bandwidth with intra-band CA as intended
For example, with a 30 MHz cell specific channel BW centered on the 100 kHz raster, it is impossible to have both a 20 and 10 MHz BWP/UE Specific channel BW also on the 100 kHz raster to support legacy UEs with a maximum 20 MHz CHBW without having the 20 and 10 MHz overlap. Overlapping CA is not supported in legacy UEs.
Observation: If UE specific CHBWs need to be centered on the 100 kHz raster, In many cases it is impossible to allow legacy UEs to use intra-band CA
30 MHz Cell specific
channel Bandwidth
20 MHz BWP
Fc= 2125 MHz
10 MHz BWP
Fc= 2134 or 2134.9 MHz
Fc=2120.5 MHz
The 10 MHz CHBW Fc cannot be in the 100 kHz raster
20 MHz BWP

## Slide 10: Issue 2: Both the Cell specific CHBW and the UE specific CHBW need to have even or odd PRBs
If one BW has an even number of PRBs and the other has an odd number, alignment of both the PRBs and the 100 kHz raster is impossible
PRB53
PRB64
5 MHz BWP or UE specific channel BW
Offset = 90+M*180=N*100 (there is no solution)
PRB52
PRB76
PRB0
PRB1
…
PRB51
PRB52
PRB53
PRB54
…
PRB104
PRB105
Cell specific channel Bandwidth (20 MHz carrier)
…
…
…
…
Fc
Fc
…
…
PRB75

## Slide 11: Issue 2: Even and odd number of PRBs
It would be very limiting if the number of PRBs in the BWPs and UE specific channel BWs had to be even if the number of PRBs in the cell specific channel BW is even, and odd if the number of PRBs in the cell specific channel BW is odd.
For example, this would prevent an operator from using a 25 MHz CHBW for newer UEs in n25 or n66 with a 20 MHz UE specific CHBW to support legacy UEs
This would also make it impossible to use a 5 MHz CHBW for RedCap in most cases since 5 MHz has an odd number of PRBs and most channel BWs have an even number
SCS (kHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 35 MHz | 40 MHz | 45 MHz | 50 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | 160 | 188 | 216 | 242 | 270
Even/odd | odd | even | odd | even | odd | even | even | even | even | even

## Slide 12: Issue 3: UE specific channels cannot be aligned with PRB0 for many combinations of channel bandwidths
Not being able to align the UE specific channel bandwidth on PRB0 leads to fragmentation of PRBs because PUCCH would be offset from PBR0
This table shows the minimum number of PRBs that the UE specific channel BW would have to be offset from PRB0 of the cell specific channel bandwidth for the UE specific channel BW to be on the 100 kHz raster

## Slide 13: Solutions that have been proposed for bands that use the 100 kHz raster
Introduce a 5 kHz raster
  Would work, but smaller raster than needed. A 10 kHz raster would be sufficient
Introduce a 10 kHz raster
  Would be sufficient to allow UE specific channel BWs to be positioned in any PRBs. Introduce a 15 kHz raster
  Would only work if the BW centered on the 100 kHz center frequency was also on the 15 kHz raster, which is effectively a 300 kHz raster rather than a 100 kHz raster
Introduce a 20 kHz raster
  Doesn’t solve the even/odd PRB issue
Introduce a 50 kHz raster
  Would fix the even/odd PRB issue, but if we are going to make a change, we should fix all the problems caused by the 100 kHz assumption for UE specific channel BWs while we are at it
Allow the UE specific channel BW to be configured on any PRBs of the SIB1 cell specific channel BW
  This is what is allowed for BWPs, and would be consistent with what many companies believed we had all along

## Slide 14: Proposal
Allow UE specific channel BWs to be positioned on any RBs of the cell specific channel bandwidth regardless of the UE specific channel BW center frequency
  This consistent with how BWPs can be configured and what most companies though was allowed prior to the RAN4 discussions in August 2022
UE specific channel BWs still need to use a number of RBs in a channel BW defined by RAN4
The network shall ensure the minimum guard band is met for each UE specific channel BW
Add a new UE capability to indicate that the UE supports UE specific channel BWs not centered in the 100 kHz raster.
The new capability would be mandatory for UEs from Rel-18 onwards, and optional for earlier UEs.
The operator would have the choice for how to handle UEs that don’t indicate the new capability IE. The gNB could be configured to use the new UE capability to either:
  Configure legacy UEs only with UE specific channel BWs on the 100 kHz raster, or
  Move legacy UEs to a different band, or carrier
  Ignore the capability, and configure UE channel BWs on any RBs within the Cell specific channel BW at their own risk
If it is deemed that 5 or 10 kHz raster (or more accurately ΔFRaster) is needed, we would support that as a means to achieve the above