## Slide 1
33GPP TSG-RAN WG4 Meeting # 111 R4-2408385
Fukuoka, Japan, May. 20th – 24th, 2024
Source: ZTE Corporation, Sanechips
Agenda Item: 13
Motivation on R19 basket WID on 4Rx support for low frquency (<1GHz) NR bands for handheld UE

## Slide 2: Backgroud
In Rel18, there are two WIDs includes FR1 band supports 4Rx operation, which are:
  WID of 4Rx_low_NR_band_handheld_3Tx_NR_CA_ENDC [1]:
    4Rx for low frequency NR bands (<1GHz) for handheld UE
      Several <1GHz bands were included: n5, n8, n20, n28, n20, n26, n71
      Related RF requirements have already been completed and included in the TS38.101-1 specification.
    It is not a basket WID, and the target completion time is RAN#102 meeting.
  WID of 4Rx_NR_bands_R18 [2]:
    4Rx for NR bands (<2.6GHz) for FWA UE, and 4Rx for NR bands (1GHz to 2.6GHz) for handheld UE
              Several <1GHz bands were included but for FWA UE: n5, n13, n26, n85
            It is a basket WID, the target completion time is RAN#103 meeting
  Reference:
  1. RP-231013, Revised WID for Low NR band 4Rx and 3Tx, OPPO
  2. RP-240251, Revised WID: Rel-18 4Rx for NR bands for FWA (Fixed Wireless Access) UEs (<2.6GHz) and handheld UEs (1GHz to 2.6GHz), ZTE, China Telecom

## Slide 3: Motivation
The impacted RF requirements for 4Rx for handheld UE and FWA UE are the same, which are the ΔRIB,4R requirements in Table 7.3.2-2 in TS38.101-1.
  All of the general RF requirements related to 4Rx for low frequency NR bands for handheld UE have already been completed.
  Supporting 4Rx in low bands for handheld UE is an optional feature.
  For a certain <1GHz band, the ΔRIB,4R requirements are different when 4Rx operation is supported by FWA form factor UE and handheld UE.
  Low frequency bands(especially <1GHz) are valuable for their large coverage but with the drawback of lower throughput due to smaller BW (typically not larger than 30MHz) and less antennas in handheld UE (now only 2Rx).
  Increasing antennas number (from 2Rx to 4Rx) can provide higher throughput and better coverage
Some demands for 4Rx for low frequency NR band for handheld UE from operators can be found in the following:
 | Contact name, company | Contact email | Other supporting companies | Additional information
n85 | Bill Shvodian, T-Mobile USA | Bill.shvodian@t-mobile.com | Ericsson, Nokia, Deutsche Telekom | Note:4Rx is for handheld UE
n13 | Yuanyuan Zhang, Samsung | tina55.zhang@samsung.com | Bell Mobility, TELUS, Nokia, Ericsson | Note:4Rx is for handheld UE

## Slide 4: Motivation(Cont’d)
Considering the demands from operators, and more low frequency NR bands may be requested by operators to support 4Rx for FWA UE and/or handheld UE in future, by using the current approach, individual WIDs will be needed for different bands, which is not an efficient way for RAN4 WIDs management.
Using Basket WID appoarch is an efficient and routine way, however, to bulit a separate basket WID only for 4Rx for low frequency(<1GHz) NR bands for handheld UE would cause redundancy and fragment due to there was already a basekt WID of 4Rx_NR_bands_R18 to do the similar work.
Therefore, it is proposed to include the low frequency (<1GHz) NR bands to support 4Rx for handheld UE in Rel-19 basket WID of 4Rx FR1 band.

## Slide 5: Proposals
Proposal 1: It is proposed to include the low frequency (<1GHz) NR bands to support 4Rx for handheld UE in Rel-19 basket WID of 4Rx FR1 band.
Proposal 2: The objection is proposed as follow:
Specify the 4Rx REFSENS requirement for NR FR1 bands
    Support of 4Rx for the bands <2.6GHz added in this WI is optional

## Slide 6: Thank you