## Slide 1: Motivation of introduction of NR based AeroMacs system
Source: ZTE Corporation, Sanechips
Agenda: 13
3GPP TSG WG RAN4#111
Fukuoka City, Fukuoka , Japan, 20th – 24th May, 2024
R4-2409627

## Slide 2: NR based AeroMACS-Use case
AeroMACS is the aeronautical mobile airport communication system (AeroMACS) which is used to provide the wireless communication system for airport to help airlines, airport authorities and airport ground service etc.
The specific ground service could be categorize as following:
Airport traffic control (ATC) and management (ATM);
Passenger and cargo airline applications;
Airport authority applcaitions (e.g. security vedio,de-icing and snow removal)

## Slide 3: Spectrum status
ITU-R WRC-07 decided to assign the 5091-5150MHz for the spectrum of AeroMACS system;
ITU-R WRC-12 decided to assign the 5030~5091MHz for the spectrum of AeroMACS system;
NAS consider the use of the 5000-5030 MHz band to extend the tuning range for the the AeroMACS.

## Slide 4: Current standarization status
AeroMACS is still using the WiMAX standard (IEEE 802.16) at the aeronautical C-band (5 GHz) to provide the service till now.
Based on the latest decision from CAAC (Civil Aviation Administration of China), it's planned to provide the NR based AeroMACS system in near future.

## Slide 5: Proposals
Proposal 1: to support the NR based AeroMACS system in Rel-19.
Proposal 2: to specify the band 5091~5150MHz for regional deployment and 5000~5150MHz for global deployment.
Proposal 3: to define RF requirement for BS and UE requirement;
Proposal 4: to define the RRM requirement for AeroMacs UE;
Proposal 5: to define the Demod requirement for AerMacs BS and UE;

## Slide 6: Thanks