## Slide 1
3GPP TSG-RAN WG4 Meeting #64 R4-124750
Qingdao, China, 13 - 17 August, 2012
Agenda item: 6
Source: TeliaSonera
Document for: Information
Vendors and operators suggestions on multi-CA issues

## Slide 2
Introduction
This input lists all the vendor and operator suggestions on how to deal with the multi-CA issues:
  Vendor A: ST-Ericsson, Ericsson
  Vendor B: Nokia, Intel, Motorola Mobility, Fujitsu, ZTE and LG Electronics
  Vendor/operator C: Qualcomm, AT&T, SK Telecom, KT
  Vendor D: RENESAS
The vendor suggestions are listed together with respect to the following points:
  Reference architecture for multi-CA issue
  Additional multi-CA relaxation applies for > xy number of CA combos
  Relaxation for multiple A1 and A2 combos
  Relaxation for multiple A3 and A1+A2+A3 combos
  Handling of overlapping bands
  Relaxation for the individual aggregated E-UTRA bands when using E-UTRA in single carrier mode or another RAT (UTRA/GERAN) in these bands
  Relaxation to E-UTRA bands which are not part of the CA bands
  Relaxation to UTRA bands which are not part of the CA bands
  Relaxation to GERAN bands which are not part of the CA bands

## Slide 3
Vendor A: ST-Ericsson, Ericsson
Inputs: R4-124553 Rel-10 CR and R4-124595 Rel-11 CR for 36.101,
R4-124687, R4-124690 Rel-9 and R4-124691 Rel-10 CR for 25.101
For each band the TIB,x is specified individually. The number “x” is related to the inter-band CA cases A1, A2, A3 and A4
Applies if number of CAs is ≥ 1
For UE(s) supporting one or several low-high combinations: a single band-specific TIB,1 for the CA and non-CA bands independent of the combination supported
  Low bands (< 1GHz) with TIB,1 no relaxation beside band 12
  High-bands (>1.4 GHz) typically TIB,1 = 0.3 dB suggested
TIB,2 the US case with low-high inter-modulation problems have 0.5 dB relaxation for the low bands (also for band 17 in the CA B4+B12?)
TIB,3 we have US cellular case with B5+B12 0.8/0.4dB and B11+B18 KDDI 0.6/0.6 dB
NOTE 1: For E-UTRA bands that are part of more than one of the E- UTRA and UTRA band combinations listed, the maximum  TIB,3 value applies
For the UE that supports one or multiple of the E-UTRA CA configurations given in Table 6.2.2-2, Table 6.2.2-3 and 6.2.2-4, the total reduction allowed for any applicable E-UTRA band is  TIB =  TIB,1 +  TIB,2 +  TIB,3 (dB)
Tries to harmonize UTRA and E-UTRA relaxation which would mean band II +IV relaxation of 1 dB would be applied to E-UTRA
Multi-RAT is FFS, but method for relaxation, and bands for which relaxations apply are consistent for E-UTRA and UTRA (with some exceptions due to legacy requirements)
No REFSENS relaxation

## Slide 4
Vendor B: Nokia, Intel, Motorola Mobility, Fujitsu, ZTE and LG Electronics
Input: R4-124375
UE supports one band combination
  Baseline MOP and REFSENS relaxations are applied only to those two bands that belong to the CA configuration. Relaxations are also applied in non-CA and UTRA mode.
  Band that are not part of the CA are not allowed to get any relaxations
UE supports more than one band combinations
  Baseline MOP and REFSENS relaxation are applied to the bands that belong to the CA configurations
  Bands that are not part of any of the CA configurations shall have ΔTIB = 0.3 dB, also in UTRA mode
  In case band belongs to multiple high-high or low-low CA configurations then MOP and REFSENS relaxations to that band are applied based on the highest baseline relaxation for that band
  In case UE supports high-low and High-high or low-low CA configurations then MOP and REFSENS relaxations to those low-low and high-high are the baseline high-high or low-low relaxation + 0.3 dB
  No relaxations to GERAN bands
This WF would close all open issues except individual baseline relaxation and impacts to radiated performance.

## Slide 5
Vendor/operator C: Qualcomm, AT&T, SK Telecom, KT
Input: R4-124630
  For the device that supports the CA configuration listed in Table 1 and only supports class A1 or A2 band combinations (i.e., does not support any high/high or low/low combinations), the RIB and TIB,c relaxations should be applied to all bands that the device supports and across UTRA and E-UTRA technologies. Additional relaxation may be needed (FFS) for the band in a class A2 combination to account for a harmonic trap filter.
  If the device does not support any of the CA configurations listed in Table 1 or if the device supports other A3 or A4 combinations, then the applicability of RIB and TIB,c relaxations to other bands and to other RAT’s is FFS.

## Slide 6
Vendor D: RENESAS
Input: R4-124317
  1) Indication of front-end class with new signaling needed
  (Comment: Problem with release independence?)
  2) CLASS1:
    For UE that supports only Low-High combinations the relaxations for all bands UE supports, including legacy and non-CA bands are Δ TIB = 0.3dB, ΔRIB=0dB. Allow certain additional Δ TIB and MSD for H3 for relevant bands
    For UE that supports also Low-low and/or High-high combinations then relaxations for those bands are calculated as a sum of 0.3dB+ ΔTIB of individual Low-Low or High-high band. For RX side the total additional loss is in many cases above 1dB that needs also relaxation. We prefer to account 100% of additional RX loss above 0.8dB. We are OK to leave ΔRIB FFS at this phase for this kind of band combinations.
  3) CLASS2:
    For UE that supports only Low-High combinations the relaxations for all bands UE supports, including legacy and non-CA bands are ΔTIB = 0dB, ΔRIB=0dB. Allow certain additional Δ TIB and MSD for H3 for relevant bands
    For UE that supports also Low-low and/or High-high combinations then relaxations for those bands are calculated as a sum of 0dB+ ΔTIB of individual Low-Low or High-high band. For RX side the total additional loss in some cases might be above 1dB that would also relaxation. We prefer to account 100% of additional RX loss above 0.8dB. We are OK to leave ΔRIB FFS at this phase for this kind of band combinations.

## Slide 7
Reference architecture for multi-CA issue
Ericsson:
  Diplexer-antenna architecture
Nokia, et al.:
  Diplexer-antenna architecture
Qualcomm:
  Diplexer-antenna architecture for low-high A1/A2 combinations
  FFS for A3 combos and/or A1, A2 and A3 combinations
RENESAS:
  Case 1 Diplexer-antenna architecture
  Case 2 Dual-feed antenna architecture

## Slide 8
Additional multi-CA relaxation applies for > xy number of CAs combos
Ericsson: If ≥ 1
Nokia, et al.: Different relaxation for single combo and xy > 1
Qualcomm: If ≥ 1 but only for low-high combos defined, others are FFS
RENESAS: Class 1 and 2 if ≥ 1

## Slide 9
Relaxation for multiple A1 and A2 combos
(Example with multi-CA B4+B13 and B3+B20, B8 GERAN, BI UTRA, B14 LTE)
Ericsson:
  A1: TIB = 0 dB for low-bands and = 0.3 dB for some high-bands
  B1: UTRA FFS for support of E-UTRA CA combination (multi-RAT FFS)
  B4: TIB = 0 dB
  B3: TIB = 0.3 dB (Note 1)
  B13, B14, B20: TIB = 0 dB
  B8: TIB = 0 dB (GERAN band no relaxation)
  RIB = 0 dB for all bands
Nokia, et al.:
  A1: TIB = 0.3 dB for low and high bands and A2 case-by-case
  B1, B3, B4, B13, B14, B20: TIB = 0.3 dB (for the CA E-UTRA and/or single carrier operation E-UTRA/UTRA case)
  B8: TIB = 0 dB (GERAN band no relaxation)
  RIB = 0 dB for all bands
Qualcomm:
  A1: TIB = 0.3 dB for low and high bands and A2 case-by-case
  B1, B3, B4, B13, B14, B20: TIB = 0.3 dB (Note 1)
  B8: TIB = 0 dB (GERAN bands no relaxation)
  RIB = 0 dB for all bands
RENESAS:
  Case 1: A1: TIB = 0.3 dB for low and high bands and A2 case-by-case
  B1, B3, B4, B13, B14, B20: TIB = 0.3 dB (Note 1)
  B8: TIB = 0 dB (GERAN bands no relaxation)
  RIB = 0 dB for all bands
  Case 2: A1: TIB and RIB = 0 dB for low and high bands and A2 case-by-case
  B1, B3, B4, B8, B13, B14, B20: TIB = 0 dB (Note 1)
  B8: TIB = 0 dB (GERAN band no relaxation)
  RIB = 0 dB for all bands
Note 1: Relaxation for the CA E-UTRA and/or single band E-UTRA/UTRA operation

## Slide 10
Relaxation for multiple A3 and A1+A2+A3 combos (1)
(Example with multi-CA B7+B20, B5+B12, B3 GERAN, BI UTRA, B4 LTE)
Ericsson:
  Single A3: TIB and RIB decided on case-by-case
  Multiple A3 combos?
  For A1, A2, A3 in A1+A2+A3 combo: Summing up the individual agreed relaxations
  B1 UTRA (multi-RAT is FFS)
  B4: TIB = 0 dB
  B7: TIB = 0.3 dB (Note 1)
  B20: TIB = 0 dB
  B5: TIB = [0.8] dB and RIB = [0.5] dB (Note 1)
  B12: TIB = [0.4] + 0.3 dB and RIB = [0.3] dB (Note 1)
  B3: TIB = 0 dB (GERAN band no relaxations)
  RIB = 0 dB for all bands except B5, B12
Nokia:
  Single A3: TIB and RIB decided on case-by-case
  Multiple A3 combos on case-by-case basis and if band belongs to multiple combos the highest baseline relaxation is selected.
  For A3 in A1+A2+A3 combo: TIB A3 + 0.3 dB and RIB A3 + 0.3 dB
  B1, B4, B7, B20: TIB = 0.3 dB (Note 1)
  B5: TIB = [0.8] + 0.3 dB and RIB = [0.5] +0.3 dB (Note 1)
  B12: TIB = [0.4] + 0.3 dB and RIB = [0.3] + 0.3 dB (Note 1)
  B3: TIB = 0 dB (GERAN bands no relaxation)
  RIB = 0 dB for all bands except B5, B12
Qualcomm:
  Single A3: TIB and RIB decided on case-by-case
  Multiple A3 combos?
  For A3 in A1+A2+A3 combo: FFS
  B1, B4, B7, B20: TIB = 0.3 dB (Note 1)
  B5: TIB = [0.8] + FFS dB and RIB = [0.5] + FFS dB (Note 1)
  B12: TIB = [0.4] + FFS dB and RIB = [0.3] + FFS dB (Note 1)
  B3: = 0 dB (GERAN bands no relaxation)
  RIB = 0 dB for all bands except B5, B12
Note 1: Relaxation for the CA E-UTRA and/or single band E-UTRA/UTRA operation

## Slide 11
Relaxation for multiple A3 and A1+A2+A3 combos (2)
(Example with multi-CA B7+B20, B5+B12, B3 GERAN, BI UTRA, B4 LTE)
RENESAS Case 1:
  Single A3: TIB and RIB decided on case-by-case
  Multiple A3 combos?
  For A3 in A1+A2+A3 combo : TIB A3 + 0.3 dB and RIB 0 dB
  B1, B4, B7, B20: TIB = 0.3 dB (Note 1)
  B5: TIB = [0.8] + 0.3 dB and RIB = [0.5] dB (Note 1)
  B12: TIB = [0.4] + 0.3 dB and RIB = [0.3] dB (Note 1)
  B3: TIB = 0 dB (GERAN band no relaxation)
  RIB = 0 dB for all bands except B5, B12
RENESAS Case 2:
  Single A3: TIB and RIB decided on case-by-case
  Multiple A3 combos?
  For A3 in A1+A2+A3 combo: TIB A3
  B1, B4, B7, B20: TIB = 0 dB (Note 1)
  B5: TIB = [0.8] dB and RIB = [0.5] dB (Note 1)
  B12: TIB = [0.4] dB and RIB = [0.3] dB (Note 1)
  B3: TIB = 0 dB (GERAN band no relaxation)
  RIB = 0 dB for all bands except B5, B12
  There is a comment in the RENESAS suggestion that if the average IL is > 1dB RIB relaxation should be considered
Note 1: Relaxation for the CA E-UTRA and/or single band E-UTRA/UTRA operation

## Slide 12
Handling of overlapping bands
(Example with multi-CA B3+B7 and B7+B20)
Ericsson: Take maximum value from the single CA A3 case if multiple A3 supported
  B3: TIB = [0.5] + 0.3 dB (Note 1)
  B7: TIB = [0.5] + 0.3 dB (Note 1)
  B20: TIB = 0 dB
Nokia: Take maximum value from the single CA case
  B3: TIB = [0.5] + 0.3 dB and RIB = 0.3 dB (Note 1)
  B7: TIB = [0.5] + 0.3 dB and RIB = 0.3 dB (Note 1)
  B20: TIB = 0.3 dB and RIB = 0 dB (Note 1)
Qualcomm:
  A3 is for FFS “but assumes diplexer-antenna architecture?”
RENESAS:
  Case 1: Take maximum value from the single CA case
  B3: TIB = [0.5]+0.3 dB (Note 1), RIB = FFS
  B7: TIB = [0.5] +0.3 dB (Note 1) , RIB = FFS
  B20: TIB = 0.3 dB (Note 1)
  Case 2: Take maximum value from the single CA case
  B3: TIB = [0.5] dB (Note 1) , RIB = FFS
  B7: TIB = [0.5] dB (Note 1) , RIB = FFS
  B20: TIB = 0 dB
Note 1: Relaxation for the CA E-UTRA and/or single band E-UTRA/UTRA operation

## Slide 13
Relaxation for the individual aggregated E-UTRA bands when using E-UTRA in single carrier mode or another RAT (UTRA/GERAN) in these bands
(E.g. B3 + B20 CA with B3, B20 in in E-UTRA single carrier mode or for UTRA/GERAN RAT)
Ericsson:
  TIB = 0 dB for low-bands and = 0.3 dB for some high-bands (exceptions may exist)
  For low-low and high-high depends on case-by-case agreement but adding additional 0.3 dB to TIB for some bands if A1/A2 is supported
  Same method of relaxation for E-UTRA and UTRA, multi-RAT is FFS
  Relaxation for GERAN bands FFS?
Nokia:
  Same as for the aggregated cases for E-UTRA/UTRA bands
    TIB = 0.3 dB for low and high-bands
    For low-low and high-high depends on case-by-case agreement
    If UE supports high-high or low-low AND low-high then case-by-case agreement + 0.3 dB to TIB and RIB
  No relaxation for GERAN bands
Qualcomm:
  TIB = 0.3 dB for low and high-bands
  For low-low and high-high depends on case-by-case agreement + possible additional relaxation which is for FFS
  Relaxation for GERAN bands FFS?
RENESAS:
  Case 1: Same as for the aggregated cases for E-UTRA/UTRA bands. No relaxation for GERAN bands.
  Case 2: low-high has 0 dB in general. For low-low and high-high the single CA agreed values are taken and applied to E-UTRA/UTRA bands. No relaxation for GERAN bands.
  General for Case 1 and Case 2: A relaxation given for certain band in inter-band configuration applies also when that band is operated in non-CA LTE.
  For instance if B7 gets 0.3+0.5=0.8dB (case1) when UE supports B3+B20 and B3+B7 then B7 in non-CA mode gets 0.8dB (case1) or 0.5dB (case2) and so on.

## Slide 14
Relaxation to E-UTRA bands which are not part of the CA bands
(E.g. B3 + B20 CA and relaxation to E-UTRA B1, B8 not part of any CA band)
Ericsson:
  TIB = 0 dB for other low-bands and TIB = 0.3 dB for some high-bands (exceptions may exist). Irrespective of number of A1 supported
Nokia:
  If number of CAs is = 1: no relaxation
  If number of CAs is > 1: TIB = 0.3 dB for other low-bands and high-bands
Qualcomm:
  TIB = 0.3 dB for other low-bands and high-bands
RENESAS:
  Case 1: TIB = 0.3 dB for other low-bands and high-bands
  Case 2: TIB = 0 dB for other low-bands and high-bands

## Slide 15
Relaxation to UTRA bands which are not part of the CA bands
(E.g. B3 + B20 CA and relaxation to UTRA BI, BVIII not part of any CA band)
Ericsson:
  TIB = 0 dB for other low-bands and TIB = 0.3 dB for other high-bands (exceptions may exist)
Nokia:
  If number of CAs is = 1: no relaxation
  If number of CAs is > 1: TIB = 0.3 dB for other low-bands and high-bands
Qualcomm:
  TIB = 0.3 dB for other low-bands and high-bands
RENESAS:
  Case 1: TIB = 0.3 dB for other low-bands and high-bands
  Case 2: TIB = 0 dB for other low-bands and high-bands

## Slide 16
Relaxation to GERAN bands which are not part of CA bands
(E.g. B3 + B20 CA and relaxation to GSM900 not part of any CA band)
Ericsson:
  No relaxation for GERAN bands
Nokia:
  No relaxation for GERAN bands
Qualcomm:
  No relaxation for GERAN bands
RENESAS:
  Case 1: No relaxation for GERAN bands
  Case 2: No relaxation for GERAN bands