## Slide 1: RFPM Way Forward
3GPP TSG-RAN WG4 Meeting #66
Malta, 28th Jan - 1st Feb
Agenda 9.5
Source: Polaris Wireless

## Slide 2
Additional LTE parameters
  UE Rx-Tx time difference measurement error model
    Follows normal distribution with zero mean
    RMS = 6Ts (assume 10Ts at 90%-ile measurement accuracy [TS 36.133])
Preliminary GSM parameters for inter-RAT
  MSR BS operating E-UTRA and GSM, total output power = 46 dBm
  Number of GSM carriers is FFS
  Detection threshold for GSM is -110dBm of carrier RSSI
  Carrier RSSI real-time measurement error model for GSM
    Follows normal distribution with zero mean
    RMS = 5.7 dB (assume 6dB at 90%-ile measurement accuracy [TS 45.008])
  Prediction and reference data error models has two components, e1+e2, each following normal distribution with zero mean
    e1: RMS = 9 dB (for 90% of randomly selected UEs)
    e2: RMS = 13 dB (for 10% of randomly selected UEs)
  The necessary GSM parameters are for further check by the next meeting. Final GSM parameters are to be agreed in RAN4#66-bis and then used for studies