## Slide 1
3GPP TSG-RAN WG4 Meeting #66 R4-130971
St. Julian’s, Malta Jan 28th – Feb 1st , 2013
Agenda item: 6.15
Source: TeliaSonera
Document for: Information
Ad-hoc on CA in multi-RAT multi-band terminals

## Slide 2
Introduction
The ad-hoc on CA in multi-RAT multi-band terminals was held on Thursday evening and the following companies were present.
TeliaSonera, Nokia Corporation, ST-Ericsson, Motorola Mobility, NTT DOCOMO, Telecom Italia, Qualcomm, Renesas, DT, Orange, Vodafone, Softbank, Fujitsu; Intel, E-Access, Huawei, ZTE, Telefonica, Samsung, LightSquared, LG Electronics, Mediatek, T-Mobile USA, Sprint, Dish CMCC, KT
It was agreed to take as a baseline:
Vendors should come back to the next meeting with an input taking the Orange/Vodafone input as a baseline. Considering the discussion as done in the New Orleans ad-hoc on that subject
In the mean time Renesas/Nokia made a revision of their document and this we can discuss first:
  R4-130453_rev2

## Slide 3
New notes to Table 6.2.5A-3: ΔTIB,c
NOTE 1: The above tolerances are only applicable for the supported E-UTRA bands that belong to the supported Inter-band carrier aggregation configurations. This excludes supported E-UTRA bands that are not supported in carrier aggregation mode.
NOTE 2: The above tolerances also apply to the supported E-UTRA bands in non-aggregated operation only if: such E-UTRA bands belong to any of the above Inter-band carrier aggregation configurations supported by the UE,.
NOTE 3: In case the UE supports more than 1 of the above carrier aggregation configurations and a E-UTRA band belongs to more than one carrier aggregation configurations then:
- If the band is ≤ 1GHz, the applicable tolerance is based on the average tolerance rounded down to closest 0.1dB that would apply for that band among the different supported carrier aggregation configurations involving such band. In case band belongs to A2, then maximum baseline relaxation among the different supported carrier aggregation configurations involving such band is applied
- If the band is >1GHz, the applicable tolerance is based on the sum of the baseline relaxations that would apply for that band among the different supported carrier aggregation configurations involving such band. An upper bound of 0.7dB is applied. If the baseline for a band combination exceeds 0.7dB, then upper bound is not applied
NOTE 4: If UE supports only multiple band combinations where lower band is below 1GHz and high band is above 1GHz then NOTE 4 does not apply

## Slide 4
Existing notes to Table 6.2.5A-3: ΔTIB,c in TS 36.101
NOTE: The ΔTIB,c in Table 6.2.5A-3 has been derived for a UE supporting a single interband LTE CA band combination. For a UE supporting additional interband LTE CA band combinations, the ΔTIB,c for all bands supported by the UE, need to be studied.
NOTE: To meet the TIB,c requirements for CA_3A-7A with state-of-the-art technology, an increase in power consumption of the UE may be required. It is also expected that as the state-of-the-art technology evolves in the future, this possible power consumption increase can be reduced or eliminated.

## Slide 5
Relaxation to UTRA bands
  The main changes are in Table 6.2.5A-3: ΔTIB,c
NOTE 3: The above tolerances also apply to UTRA bands that correspond to the E-UTRA bands that belong to the supported Inter-band carrier aggregation configurations [and the E-UTRA band is over 1 GHz]
Nokia: belongs only to the UTRA bands which are in the inter-band CA
Vodafone: We can not agree as it was not in the original proposal
TeliaSonera: can we have exceptions for low bands
Qualcomm prefers not to have exceptions
Telecom Italia: Does not accept
Orange: Same as Vodafone and Telecom Italia.
Renesas: Band 8 in Europe is in question. B8 + B20 loss is 0.8 dB
DT: Could compromise on that and also TeliaSonera
WF: No WF agreed

## Slide 6
Relaxation for multi-CA E-UTRA bands ≤ 1 GHz
Renesas/Nokia:
  The main changes are in Table 6.2.5A-3: ΔTIB,c
In case the UE supports more than 1 of the above carrier aggregation configurations and a E-UTRA band belongs to more than one carrier aggregation configurations then:
- If the band is ≤ 1GHz, the applicable tolerance is based on the average tolerance rounded down to closest 0.1dB that would apply for that band among the different supported carrier aggregation configurations involving such band. In case band belongs to A2, then maximum baseline relaxation among the different supported carrier aggregation configurations involving such band is applied
NOTE 5: If UE supports only multiple band combinations where lower band is below 1GHz and high band is above 1GHz then NOTE4 does not apply
DOCOMO: E.g. if we have A2 with 0.8 dB relaxation do we have upper cap?
Nokia: In that case the relaxation is what it specified in the table for the low-high A1
Vodafone: Not happy and would need more time.
Renesas: Excluding the AT&T combination the difference is rather small for other CA combinations. It influences mainly combinations outside Europe.
TeliaSonera would be acceptable
WF: No way forward agreed. This is mainly as the vendors also want to apply the relaxation to the corresponding UTRA bands of the inter-band CA .

## Slide 7
Relaxation for multi-CA E-UTRA bands > 1 GHz
(influences overlapping bands!)
Renesas/Nokia:
  The main changes are in Table 6.2.5A-3: ΔTIB,c
In case the UE supports more than 1 of the above carrier aggregation configurations and a E-UTRA band belongs to more than one carrier aggregation configurations then:
If the band is >1GHz, the applicable tolerance is based on the sum of the baseline relaxations that would apply for that band among the different supported carrier aggregation configurations involving such band.
An upper bound of 0.7dB is applied. If the baseline for a band combination exceeds 0.7dB, then upper bound is not applied
NOTE 5: If UE supports only multiple band combinations where lower band is below 1GHz and high band is above 1GHz then NOTE 4 does not apply
Vodafone: To take only the max value for that combination.
Nokia: LTE band in single band mode if the relaxation can be applied below 1GHz. Note 2 in the Renesas/Nokia input
Telecom Italia: We have to look onto the whole picture. The max could be considered as proposed

## Slide 8
Relaxation for multi-CA E-UTRA bands > 1 GHz
(influences overlapping bands!)
Renesas/Nokia:
  The main changes are in Table 6.2.5A-3: ΔTIB,c
In case the UE supports more than 1 of the above carrier aggregation configurations and a E-UTRA band belongs to more than one carrier aggregation configurations then:
If the band is >1GHz, the applicable tolerance is based on the sum of the baseline relaxations that would apply for that band among the different supported carrier aggregation configurations involving such band.
An upper bound of 0.7dB is applied. If the baseline for a band combination exceeds 0.7dB, then upper bound is not applied
NOTE 5: If UE supports only multiple band combinations where lower band is below 1GHz and high band is above 1GHz then NOTE4 does not apply
Vodafone: It is not good to have for single E-UTRA the same relaxation
Nokia: Not possible as this would also mean in CA E-UTRA we can not have the relaxation. Is there any operator which could agree on the proposal now.
TeliaSonera: If we modify the <1GHz to get no relaxation for some bands is it than acceptable? Docmo almost, DT seriously consider it,
WF: No WF agreed. Renesas/Nokia will have a new version with removing the sum and upper cup as proposed above and instead to allow only to use the max value.