## Slide 1: FeICIC interference estimation under signaling
Qualcomm
R4-133450
3GPP TSG-RAN WG4 Meeting #68
Barcelona, Spain, 19 - 23 August, 2013
Agenda Item: 7.8.2

## Slide 2: Introduction
In this paper we provide
  Clarification regarding when the network expects UE to perform FeICIC interference estimation
    Relevant only for ABS subframes and under colliding-CRS
Note that
  Our proposal does not restrict CRS-IC in any manner.
    We note that CRS-IC is beneficial even in non-ABS subframes.
      UE can always perform CRS-IC (whether ABS or non-ABS) to remove non-colliding CRS impact, improve channel estimation under colliding CRS, and improve measurement accuracy
  Our proposal does not mandate certain UE behavior on non-ABS or complimentary subframes.
  Our proposal is not related to non-colliding CRS.
  Our proposal is not related to measurements.
The UE’s interference estimation affects CSI, RLM, and demod.

## Slide 3: RAN2 description is not clear
  When the received CRS assistance information is for a cell with CRS colliding with that of the CRS of the cell to measure, the UE may use the CRS assistance information to mitigate CRS interference (as specified in [FFS]) on the subframes indicated by MeasPCell, measSubframePatternConfigNeigh and csi-MeasSubframeSet1. Furthermore, the UE may use CRS assistance information to mitigate CRS interference from the cells in the IE for the demodulation purpose as specified in [FFS].
Just talks about mitigating CRS interference
Not clear what UE should assume for interference estimation

## Slide 4: UE’s interference estimation
“FeICIC interference estimation”
  Intended for signaled (“ABS”) subframes
  Remove aggressor’s contribution via CRS-IC and estimate only residual.
  Required to meet FeICIC CSI, RLM, and demod performance
“Regular interference estimation”
  Intended for non-ABS subframes
  Implementation specific
  Advanced interference estimation techniques such as blind Nt estimation is not precluded
Wrong application of interference estimation creates mismatch in CSI and RLM and may severely degrade demod performance.
Bottom line: UE has to know which of the above two interference estimations should be applied
  Rel-11 UE is not required to blindly determine whether a given subframe is “ABS”.
  Rather, Rel-11 UE relies on signaling.
  Therefore, there should be a clear rule to guide UE regarding when to apply “FeICIC interference estimation”.
When does UE have the “green light” to do “FeICIC interference estimation”?

## Slide 5: Non-ambiguous Cases
As long as measSubframePatternPCell is configured on csi-MeasSubframeSet1, it is clear to UE which interference estimation to apply.

## Slide 6: Ambiguous Case #1
UE has colliding-CRS aggressor. Both CSI subset and measSubframePatternPCell are configured. However, measSubframePatternPCell is configured on csi-MeasSubframeSet2.
  Our view: some network may use such configuration to perform measurements on non-ABS. However, measSubframePatternPCell should not trigger “FeICIC interference estimation”, as the subframes belonging to measSubframePatternPCell belong to csi-MeasSubframeSet2. CSI and RLM on subframes belonging to measSubframePatternPCell should be based on “regular interference estimation”.

## Slide 7: Ambiguous Case #2
UE has colliding-CRS aggressor. measSubframePatternPCell is configured, but CSI subset is not configured
  Our view: similarly to case #1, this should not trigger “FeICIC interference estimation”, as there is no CSI subset configured. CSI and RLM should be based on “regular interference estimation”.

## Slide 8: Proposal
FeICIC interference estimation
  In the case of colliding CRS, UE shall perform interference estimation based on the following criteria:
    On subframes indicated by csi-MeasSubframeSet1, UE performs “ABS interference estimation”.
    On other subframes, UE performs “regular interference estimation”, where advanced interference estimation techniques such as blind Nt estimation is not precluded.
  Example
    measSubframePatternPCell is not a trigger for “ABS interference estimation”. measSubframePatternPCell is used simply to enable restricted measurements and improve measurement accuracy via CRS-IC.
Note: CRS interference mitigation could be performed for demodulation enhancements on all subframes.