## Slide 1: Way Forward on NAICS receivers
MediaTek, Orange, Verizon Wireless, Intel, Samsung, Huawei, Qualcomm, Ericsson, LGE, Blackberry, Renesas, Broadcom, NTT DoCoMo
3GPP TSG RAN WG4 #68 R4-134454
Barcelona, Spain, August 19-23, 2013
Agenda item: 10.6

## Slide 2: Current status in RAN4
Phase-1 (Calibration) study assumes fixed ON/OFF pattern of the two explicitly modeled interferers, and with fixed MCS of the serving cell
  Phase 1 studies are ongoing
Phase-2 study assumes dynamic ON/OFF modeling of the two explicitly modeled interferers (e.g., MCS/RI/PMI), and with adaptive or fixed MCS of the serving cell
  Phase 2 modeling discussions are ongoing and evaluations results are pending

## Slide 3: Observations of NAICS Receivers
  Based on Phase-1 (Calibration) study only, for Scenario 1
Company results so far showed that nonlinear receivers (i.e., ML/R-ML, SLIC, and CWIC) can provide significant performance gain over baseline LMMSE-IRC in some cases
    The above NAICS receivers were studied under the assumption of known interferer parameters (additionally for CWIC perfect PDSCH allocation alignment is assumed). Evaluation of some receivers was also performed with blind and partially blind detection.
Performance gain was also observed for linear receivers (E-LMMSE-IRC and WLMMSE).
  The E-LMMSE-IRC receivers was studied under the assumption of known interferer parameters.
  The WLMMSE receiver was studied under the assumption of PAM transmission from the dominant interferer.
Performance gain significantly depends on interference condition and MCS/RI, transmission mode, and quality of the channel estimation of serving and interference cells. Generally, the gain increases with increased I/Noc.
Candidate NAICS receivers will have different trade-offs between performance, complexity, network coordination, and network signalling. Details are yet to be studied.
The list of candidate receivers under evaluation in RAN 4 as well as the associated terminology is provided in the attached TP

## Slide 4: Next-step in RAN4
RAN4 continues to study the performance comparison among NAICS receivers, especially:
  Phase 2 modelling details
  Complete link evaluations of Phase-1 and Phase 2
    With network assistance, full blind detection and partially blind detection of interferer parameters
  Performance dependency on interference condition, network coordination and/or signalling, as well as on the reliability of parameter detection in the case of blind or partially blind detection.

## Slide 5: System Level Evaluation
The performance of NAICS receivers should be evaluated from both link level and system level perspective, in RAN4 and RAN1 respectively.
  RAN1 will study system level modelling methods to take into account performance-affecting factors (e.g., interference condition, coordination assumptions, signalling requirements, channel estimation, interferer parameter blind or partially blind detection) for candidate NAICS receivers with the input of RAN 4

## Slide 6: LS to RAN 1
  Send an LS to RAN1 in RAN#68 based on the WF
  Proposed Action:
  RAN 4 respectfully asks RAN 1 to take the above information into account to start discussion on the objective #3 as described in the SID, for the receivers identified in RAN4