## Slide 1: Summary on feasibility study of TDD eIMTA
CATT , NSN, Nokia Corporation, Inter Corporation , Ericsson , Huawei
R4-141674
TSG-RAN WG4 Meeting #70bis
San Jose Del Cabo, Mexico, 31 March – 04 April 2014
Agenda Item: 7.6.1

## Slide 2: Observations based on RAN4 feasibility evaluation results
For CCIM
  In Scenario 3, co-existence feasibility criteria is fulfilled when CCIM mechanism is applied with proper threshold.
  In Scenario 4, co-existence feasibility criteria is fulfilled when CCIM mechanism with proper threshold is applied on Pico layer and when Macro BSs are operating in UL transmission direction.
  In Scenario4, co-existence feasibility criteria is not satisfied when Macro BSs operate in DL transmission direction and Pico cells receive UL signals even with CCIM scheme. However, throughput gains still can be achieved compared with no IM case. One company observed that there are no throughput and geometry outage problems in R4-140604.
For UL PC
  Improvement of both cell average and cell edge throughput observed compared with the no IM case
  Due to diverse results and different ULPC parameter settings no consensus was reached on whether the feasibility criteria can be met.
  When CCIM and UL PC IM are applied together, the co-existence feasibility criteria is fulfilled for Scenario 3 when proper CCIM threshold and ULPC settings are applied. One company observed that CCIM threshold could be relaxed with UL PC according to the results in R4-142181. Using joint CCIM and UL PC IM mechanisms in Scenario 4 was not studied.
Impact on specification
  No impact on RAN4 core specification based on current feasibility evaluations.
  Note : it is recommended that the feasibility evaluations be taken into account in eIMTA implementation by operator.

## Slide 3: Reference
R4-137142, Simulation assumptions for feasibility study of TDD eIMTA
R4-140118 Huawei
R4-140604 Intel Corporation
R4-140646 NSN, Nokia Corporation
R4-140769 Ericsson
R4-140810 CATT
R4-141468 Ericsson
R4-141516 Intel Corporation
R4-141688 Huawei
R4-142181NSN, Nokia Corporation
R4-142182 NSN, Nokia Corporation