## Slide 1: Way Forward for PRS Signal Levels in RSTD Delay Test Cases
Alcatel-Lucent, Ericsson, Intel, Huawei
R4-142523

## Slide 2: Background
RSTD reporting delay test cases in TS 36.133 are defined with ETU30 fading channel with some added margins on the performance requirements
The PRS signal strength for RSTD accuracy requirements were defined based on previous simulation results
In [R4-141444], it was argued that UE might have difficulty to pass the reporting delay test cases because the signal after the fading channel is not high enough to guarantee the signal detection
  In [R4-141444], it has been proposed that PRS signal strength for reporting delay test cases is increased by 12dB in order to maintain a high enough detection probability of the PRS signals

## Slide 3: Way Forward
Examine whether the PRS signal strength for reporting delay test cases are properly defined with new simulation
The parameters defined in the RSTD reporting delay test cases will be used for the simulation (see Table A.8.12.1.1-3 in TS 36.133)
  the detection thresholds should be calibrated based on the current measurement accuracy requirements (Es/Iot=-6dB for serving, Es/Iot=-13dB for neighbour cells)
Additionally, the following PRS signal strengths may be used for the simulation:
  PRS Es/Noc for Cell 1 and Cell 2
    {-4, -10} as defined in Table A.8.12.1.1-3 already
    {-2, -8}, {0, -6}, {2, -4}, {4, -2}, {6,0} additional simulations
    Note: To minimize simulation effort, if the probability of the misdetection for a pair of PRS signal strength parameters already less than 5%, there will be no need to provide the simulation results for the PRS signal parameters with stronger PRS signal strengths
  Other settings are not precluded
Simulation results to be collected:
  The probability of the detecting/not-detecting PRS (no RSTD measurements)
  The accuracy for RSTD measurements
Simulation results with the same settings for AWGN should also be presented
PRS signal strength for reporting delay test may be adjusted if the simulation results show the probability of the PRS detection of current test cases is lower than 90%.