## Slide 1: 1+7 Way forward
[Vodafone]
RAN4 #72 Dresden R4-145553
Vodafone
Approval

## Slide 2: Background: from ad-hoc meeting minutes in R4-14XXXX
 | ∆T | ∆R
B1 | 0.5 | 0
B7 | 0.5 | 0
 | ∆T | ∆R
B1 | 0.4 | 0
B7 | 0.5 | 0.1
 | ∆T | ∆R
B1 | 0.4 | 0
B7 | 0.6 | 0
 | ∆T | ∆R
B1 | 0.5 | 0
B7 | 0.6 | 0
 | ∆T | ∆R
B1 | 0.5 | 0.1
B7 | 0.7 | 0.2
 | ∆T | ∆R
B1 | 0.5 | 0
B7 | 0.7 | 0.2
 | ∆T | ∆R
B1 | 0.4->0.5 | 0
B7 | 0.5->0.7 | 0->0.2
E-UTRA bands | IL (dB) | IL (dB) | IL (dB) | IL (dB) | IL (dB) | IL (dB) |  |  | AVG
1 Tx | 0,4 | 0,7 | 0,4 | 1,32 | 0,85 | 1,1 |  |  | 0,795
1 Rx | 0,5 | 0,7 | 0,2 | 1,23 | 0,98 | 0,7 |  |  | 0,718333
7 Tx | 0,3 | 1,2 | 0,7 | 1,41 | 1,02 | 1,2 |  |  | 0,971667
7 Rx | 0,8 | 1,2 | 0,4 | 1,55 | 0,84 | 0,8 |  |  | 0,931667
UPDATED and CORRECTED
Chair summary
Notes: Delta R B1
Chair: propose to use deltaR as 0dB for band 1
QCM: we would like to see the final set. No problem to discuss individually
deltaT B1
Chair: for B1 Tx propose to use 0.4 based on IL?
QCM: our proposal is 0.5 based on previous A2 combinations
Telecom Italia: approach from QCM based on avg should not be followed. It should be case by case. Support 0.4
Intel: more difficult to achieve output power than better ref sens. Support 0.5
QCM: VF proposed 0.5
VF: that was compromise based on rest of IL
B7 Tx:
Chair: would be acceptable to use 0.6 as compromise?
QCM: we prefer 0.7dB
TIM: pure shared pain, 1dB-> 0.5dB, 0.6cannot be accepted
LGE: suggest to remove LG Uplus
Chair: is QCM willing to compromise?
QCM: B1 should 0.5 as VF also agrees to 0.5
LGE: deltaR in B1 is also compromised. B1:delta T 0.5, and B1 R=0
B7 Rx
VF: ok to compromise on Rx to be 0.1dB
TIM: margins on Rx side are huge. deltaR should 0 for Band 7. from intel refsens is easier than tx. We should cosnider diff approac for deltaT
Orange: based on emasurements there are margins
Intel: share pain should 0.5. support 0.2
Chair: is QCM against 0.1
QCM: we support 0.2
Chair summary:
B1: deltaT: 0.4->0.5dB deltaR:0dB
B7: deltaT: 0.5->0.7dB deltaR: 0->0.2dB

## Slide 3: WF
The following relaxations are agreed as a compromise
 | ∆T | ∆R
B1 | 0.4 | 0
B7 | 0.6 | 0.1