## Slide 1: Consideration on test patterns for PUSCH requirements
NTT DOCOMO, INC.
R4-147253
Agenda 7.6.2
3GPP TSG-RAN WG4 Meeting #73
San Francisco, Nov 17 – 21, 2014

## Slide 2: Background
Previous discussion
  In [1]R4-146687, test patterns for BS PUSCH requirement was discussed for CA.
However, before discussing for supporting CA patterns, it was identified either non CA case, FDD-FDD CA only case or TDD-TDD CA only case is not clear in our analysis.
This contribution clarifies what is not clear and shows our understanding.

## Slide 3: Current Requirement
TS36.141 section 8.2.1.1 [2]
  For a BS supporting multiple channel bandwidths and not supporting carrier aggregation only the tests for the lowest and the highest channel bandwidths supported by the BS are applicable.
  For a BS supporting carrier aggregation only the CC combination with largest aggregated bandwidth and the largest number of component carriers is used for the test. For this CC combination the tests using full PRB allocation FRC are conducted on per CC basis and measured by the required SNR levels corresponding to the bandwidths used on the different CCs.

## Slide 4: Issues in 1st paragraph(1/2)
Q1) Is this description considered as each band or all supporting bands ?
  Ex) for a BS supporting B_a(5M, 10M, 15M, 20M), B_b(5M, 10M, 15M, 20M), B_c(5M, 10M, 15M, 20M), which is applicable?
    B_a(5M,20M), B_b(5M,20M), B_c(5M,20M) : 6tests
    B_x(5M), B_y(20M) : 2tests # x, y = Either a, b or c
: our understanding
  For a BS supporting multiple channel bandwidths and not supporting carrier aggregation only the tests for the lowest and the highest channel bandwidths supported by the BS are applicable.
To test all bands, it should be considered as each band.

## Slide 5: Issues in 1st paragraph(2/2)
Q2) Which does “carrier aggregation” mean?
  Intra band CA only
  Intra/inter band CA
  Ex) for a BS supporting B_a, B_b and CA_a-b, which is applicable?
    This requirement is applied to this BS, which is not supporting “CA”.
    This requirement is NOT applied to this BS, which is supporting “CA”.
: our understanding
  For a BS supporting multiple channel bandwidths and not supporting carrier aggregation only the tests for the lowest and the highest channel bandwidths supported by the BS are applicable.
To test all bands, it should mean Intra band CA only.
(The details are shown in slide 7th and 11th.)

## Slide 6: Issues in 2nd paragraph(1/2)
Q3) Which is dominant?
  largest aggregated bandwidth
    Since the test with the larger bandwidth can be done,
  largest number of component carriers
  Ex) for a BS supporting CA_a(20+20MHz) and CA_b(10+10+15MHz), which is applicable?
    CA_a(20+20MHz) is used for the test.
    CA_b(10+10+15MHz) is used for the test.
  For a BS supporting carrier aggregation only the CC combination with largest aggregated bandwidth and the largest number of component carriers is used for the test. For this CC combination the tests using full PRB allocation FRC are conducted on per CC basis and measured by the required SNR levels corresponding to the bandwidths used on the different CCs.
To capture larger bandwidth characteristics,
“The larger bandwidth” should be prioritized.
: our understanding

## Slide 7: Issues in 2nd paragraph(2/2)
Q4) Should tests be done for any band which is not included in the CC combination?
  Ex) for a BS supporting B_a, B_b, B_c and CA_a-b, is the test for B_c done?
    No, the test for B_c is NOT applicable.
    Yes, the test for B_c is applicable.
  For a BS supporting carrier aggregation only the CC combination with largest aggregated bandwidth and the largest number of component carriers is used for the test. For this CC combination the tests using full PRB allocation FRC are conducted on per CC basis and measured by the required SNR levels corresponding to the bandwidths used on the different CCs.
: our understanding
To test all bands, “CC combination” should be considered as Intra band CA only.

## Slide 8: Corresponding Recommendations
R1) Clarify that tests should be done for all supporting bands.
R2) Clarify that “carrier aggregation” means “Intra-band carrier aggregation”.
R3) Clarify that “largest aggregated bandwidth” is prior to “largest number of CCs”.
R4) Test(s) should be done for any band which is not included in the CC combination is already covered by R1.

## Slide 9: Summary
PUSCH test should be done for all supporting Bands.
(The flow chart below should be applied to each Bands)
1st paragraph is applied to
this Band.
Does this Band support
Intra-band CA?
No
one
2nd paragraph is applied to
this CC combination.
Select a CC combination with the largest number of component carriers within them
two or more
Yes
number of CC combinations
with largest aggregated bandwidth
Start

## Slide 10: Annex(1/2)
Ex) BS supporting B_a(5M, 10M, 15M, 20M), B_b(10M, 15M)
  Following our recommendation
  Not following our recommendation
 | Channel bandwidth |  |  | 
 | 5MHz | 10MHz | 15MHz | 20MHz
B_a | * | - | - | *
B_b | N/A | * | * | N/A
* : Test done
- : Test not done
 | Channel bandwidth |  |  | 
 | 5MHz | 10MHz | 15MHz | 20MHz
B_a | * | - | - | *
B_b | N/A | - | - | N/A
No tests for B_b are done
Tests for B_b are done

## Slide 11: Annex(2/2)
Ex) BS supporting B_a, B_b, B_c, B_d and 3 CA combinations as below
  Following our recommendation
    Tests for all bands are done.
  Not following our recommendation
    Only the test for B_d with 3CC(60MHz) is done.
      Tests for B_a, B_b and B_c (marked as RED) are not done as CA_d has “largest aggregated bandwidth and the largest number of component carriers.”
Band | Bandwidth(MHz) |  | CA combination |  | 
 |  |  | CA_a-b | CA_a-c | CA_d
 | Max | Min | Maximum aggregated bandwidth [MHz] |  | 
 |  |  | 40 | 35 | 60
B_a | 20 | 5 | 1CC | 1CC | -
B_b | 20 | 5 | 1CC | - | -
B_c | 15 | 10 | - | 1CC | -
B_d | 20 | 10 | - | - | 3CC

## Slide 12: Reference
[1] R4-146687, “Way Forward on BS Performance Test Requirements for CA”, Alcatel-Lucent
[2] TS36.141 v12.5.0