## Slide 1: WF on D2D RMC performance evaluation for future meeting
Qualcomm Incorporated
R4-151066
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, Feb. 9th – Feb. 13th, 2015

## Slide 2: Background
In RAN4#74, simulation results for D2D RMC for REFSENS was provided by companies
  Results are summarized in R4-151062
  Large span was observed in the results
    PSDCH : Span of 1.24dB
    PSSCH (10MHz) : Span of 1.97dB
    PSSCH (5MHz) : Span of 2.22dB
It was agreed that Companies are encouraged to further discuss the simulation assumptions and provide second round of results for the next meeting.
The aim of this WF is to align the simulation assumptions for further alignment

## Slide 3: Proposals
Proposal 1: Rapporteur to initiate email discussion to align simulation results
Proposal 2: Companies encouraged to provide alignment results for the following scenarios to identify any difference in simulation assumptions
Case | D2D channel | Time offset | Frequency offset | Channel | HARQ Retransmissions | Time/Frequency offset estimation and compensation
1 | PDSCH | 0 us | 0 Hz | AWGN | 0 | {No, Yes}
2 | PSSCH (5MHz) | 0 us | 0 Hz | AWGN | 0 | {No, Yes}
3 | PDSCH | 0 us | 0 Hz | EVA | 0 | {No, Yes}
4 | PSSCH (5MHz) | 0 us | 0 Hz | EVA | 0 | {No, Yes}
5 | PDSCH | Tx: 0 Rx: +23Ts | Tx: 0 Rx: 200Hz | AWGN | 0 | {No, Yes}
6 | PSSCH (5MHz) | Tx: 0 Rx: +23Ts | Tx: 0 Rx: 200Hz | AWGN | 0 | {No, Yes}
7 | PSSCH (5MHz) | 0 us | 0 Hz | AWGN | 3 | {No, Yes}
Note: For PSDCH (2RBs transmission BW), 5MHz channel BW will be used

## Slide 4: Proposals
Proposal 3: Companies encouraged to provide the results for the agreed RMC for D2D REFSENS again in RAN4 #74bis
  Reuse simulation assumptions agreed in RAN4#73 and #74 in R4-148062 and R4-151093