## Slide 1: Way Forward on CSI reporting under NAICS
Ericsson, Nokia Networks, Nokia Corporation, Intel, LG, NVIDIA

## Slide 2: Background
NAICS WI is planned to be completed in June 2015
RAN4 has been tasked to verify the feasibility of the current CQI definition in the context of NAICS.
RAN 4 discussed several options in terms of CQI computation i.e.
  CQI computed based on LMMSE-IRC
  CQI computed based on LMMSE-IRC+CRS-IC (partial post-NAICS)
  CQI computed based on a semi-static approach (partial post-NAICS)
  CQI computed based on dynamic post NAICS (full post-NAICS)

## Slide 3: Way forward
RAN 4 acknowledges that the UE is capable of computing CQI based on LMMSE-IRC
  Tests are already available to verify this behaviour (type A receiver tests)
  FFS if new tests are required to account for NAICS conditions
RAN 4 acknowledges that the UE is capable of computing CQI involving CRS-IC with the configuration of measurement set
  The behaviour is verified under feICIC.
RAN4 has not verified the CQI computation involving CRS-IC in non-FeICIC cases.
Under the agreement of 3 layers cancelled by the UE under NAICS, and in particular in the absence of serving cell PDSCH for the intended UE, RAN4 does not have consensus on the feasibility of the CQI computation based on dynamic post NAICS

## Slide 4: Way forward
In the next meeting the companies are expected to provide analysis on the enhanced CQI reporting solutions (listed below) and their comparison with LMMSE-IRC based CQI reporting
  CQI calculation based on LMMSE-IRC+CRS-IC
  CQI calculation based on a semi-static approach
  Other options are not precluded
For Rel-12 NAICS RAN 4 can adopt only CQI reporting based on solutions that are agreed to be feasible.
  Whether an LS to RAN 1 is required is FFS.

## Slide 5: Which analysis to provide
Recommendations for the analysis
  INR@50%tile and 80%@tile,
  EPA5 (or static channel conditions)
  Varying (modulation, rank, etc.. ) interference
  At least 2 cases
    TM4/4/4, colliding CRS case with RI=1 in serving cell.
    TM9/9/9, non colliding CRS case with RI=1 in serving cell
  Results in terms of tput vs SNR with follow CQI
  Initial results can be considered with wideband CQI reporting.
  Full and partial loading for serving and interfering cell could be considered
    Multiple levels of serving and interfering cell loading
  Other conditions are not precluded
  Companies are welcome to provide results with and without OLLA
    If OLLA is included, details should be provided.
    Companies are encouraged to discuss OLLA details in the reflector before next meeting.