## Slide 1: Way forward on Region 1 MSS band
NTT DOCOMO, INC., KDDI, DISH, Solaris Mobile, KT, Nokia Corporation, LGE, Nokia Networks, Sony Mobile, Ericsson
R4-151276
3GPP TSG-RAN WG4 Meeting #74
Athens, Greece, 10th to 14th, February 2015

## Slide 2: Way forward
  The following is agreed as a package
  A 2x90 band plan is agreed [BXXX] 1920-2010 // 2110-2200MHz
  The duplexer assumption for [BXXX] requirements specification will be
    The lower duplexer is LTE Band 1 (2x60MHz)
    The upper duplexer is 2x90MHz
  For a UE that supports both LTE Band 1 and the new band [BXXX], no relaxation is allowed for Band 1 when all the carrier(s) are located within Band 1 operating frequency range
  For BXXX, we study the specification impact of the following approaches:
    Specifying requirements based on channel bandwidth assignment (e.g. when all the channel bandwidth(s) is confined within LTE Band 1 frequency range, at least the Band 1 requirements apply)
    UEs that support the new band [BXXX] shall also support LTE band 1 and all its capabilities
    Other approaches are not precluded

## Slide 3: Background
There are four contributions[1-3]. Specifically, in [1], there are following proposals.
  A dual duplexer UE implementation is assumed for a 2x90MHz band, where
    The lower duplexer is LTE Band 1 (2x60MHz)
    The upper duplexer is TBD
  LTE Band 1 performance within 1920-1980/2110-2170MHz is kept with a 2x90MHz band plan with the dual duplexer as above
  When any channel bandwidth(s) are confined within LTE Band 1 frequency range, the same requirements as those for LTE Band 1 shall be applied to the new band.
  Any relaxation for LTE Band 1 coming from the new band shall not be allowed.
    Ex: “For a UE that supports both LTE Band 1 and the new Band, XXX requirement is relaxed by YYY
  UEs that support the new band shall also support LTE Band 1 RF requirements and signaling requirements.
    Applying proposal 3 to the new band in addition to proposal 5 is FFS.

## Slide 4: Reference
R4-150182:
  Band plan for 2 GHz band in Region 1, DISH Network, Solaris Mobile Ltd.
R4-150564:
  A way forward on 90MHz band plan, Nokia Networks, Nokia Corporation
R4-150406:
  Way forward on MSS band, NTT DOCOMO, INC.