## Slide 1: WF on NAICS CQI Reporting
Qualcomm, Huawei, NTT DOCOMO, MediaTek, [],…..
3GPP TSG RAN WG4 #74bis
Rio de Janeiro, Brazil, 20th – 24th April 2015
Agenda item 6.6.2
R4-152371

## Slide 2: NAICS CSI Reporting
RAN4 considers the performance and complexity of CQI reporting algorithms for NAICS CQI reporting
  Complexity of MMSE-IRC based CQI reporting is feasible for CQI reporting
  RAN4 acknowledges that, in some scenarios, the MMSE-IRC based CQI may under-report the CQI compared to NAICS demod BLER
RAN4 has determined that MMSE-IRC based CQI reporting is allowed for Rel-12 NAICS

## Slide 3: CQI Testing in RAN4
CQI test cases to be defined to ensure the following
(1) CQI robustness: CQI tested by RAN4 preserves NAICS demodulation gains compared to MMSE-IRC based demodulation
(2) CQI minimum gain test: The performance of NAICS demod with the tested CQI is at least as good as MMSE-IRC based CQI reporting

## Slide 4: Way forward
Companies are encouraged to provide evaluation results for “CQI Robustness test” in [RAN4 reflector by xx/xx]
  Minimum requirement set based on assumption of MMSE-IRC CQI report
  Details of simulation assumption will be provided in [RAN4 reflector by yy/yy from zzz]
Interested companies are encourage to provide detail of CQI estimation scheme and it’s analysis for “CQI Minimum Gains test”
  LS to RAN1 will be discussed based on above analysis in the next meeting

## Slide 5: Concept of CQI Robustness Test
Verification of no performance loss compared with MMSE-IRC
  Use a structured interference (Prior agreed randomized model comprising R1/R2 & 4/16/64 QAM) with HIGH and LOW INRs:
    HIGH: INR1 = 13.91 dB, INR2 = 3.34 dB
    LOW: INR1 = 3.28 dB, INR2 = 0.74 dB
  Requirements (Check relative throughput with follow CQI )
      Gamma = Throughput_NAICS / Throughput_IRC
      Gamma >= [1.0] on operating SINR in both HIGH and LOW interference conditions
[Verification of unified CQI reporting under same interference condition]
  Interested companies are encourage to provide detail of this test in [RAN4 reflector by yy/yy]

## Slide 6: Concept of CQI Minimum Gains Test
Verification of CQI reporting capturing minimum post NAICS gains
  Step 1: Use unstructured Gaussian interference with HIGH INR
    With follow CQI, this yields a throughput of T2
  Step 2: Use a structured interference (Prior agreed randomized model comprising R1/R2 & 4/16/64 QAM) with HIGH INR
    With follow CQI, this yields a throughput of T1
  Step 3: Gamma = T1/T2
  Step 4: Check Gamma value versus requirements
    Gamma >= [1.0] on operating SINR point