## Slide 1: Motivation for New Band 41 UE power class
RP-152756 Motivation on Band 41 TDD Power Class 1

## Slide 2: Higher UL UE Tx Power Increases Band 41 Coverage
Band 41 coverage is UL limited
  Data (1 Mbps DL, 256 kbps UL) link budget is UL limited as shown in TR 36.824
  Planet Simulation shows ~30% increase in B41 coverage area from 3dB increase in UL Power
3dB
UL @
+23 dBm
UL @ +26 dBm
DL

## Slide 3: UE UL Tx Power Increase Enabling Technologies
  “Boost” Envelope Tracking allows increased PA_out with similar linearity with same battery supply voltage
  Multi-Stage Amplifiers allows higher power while mitigating thermal issues from single PA
  Implementation of flexible B41 FBAR Filters would allow for reduced insertion losses
  New RF switches with higher linearity and lower insertion loss (e.g. MEMS)
  Optimized RF Front End B41 Tx chain to reduce insertion losses

## Slide 4: Regulatory Considerations
In the US market there are two factors that limit a UE’s output power
  Specific Absorption Rate (SAR)
    FCC has specific requirements to protect public health.
    Based on the FCC test reports most of current Band 41 devices pass FCC SAR testing (<1.6 W/kg) with comfortable margin
    SAR mediation is implementation specific
  Out of Band Emissions / ACLR
    Analysis of FCC Certification reports shows current Sprint devices meeting OOBE limits with comfortable margins (~7-8 dB)
    Analysis of detailed data from a tier 1 RF Front End vendor shows 8 dB margin (worst case) for OOBE limits when operating at +23 dBm (at antenna connector)
    Consultations with vendors indicate that higher powers (+26 dBm, or more) within current emissions limits are definitely possible with PA linearization techniques such as EnvelopTracking.

## Slide 5: Implementation Aspects
Power Consumption / Battery Life not significantly impacted
  Most smartphone power is used for App Processor and Display.
  Theoretical extrapolation analysis suggests +3 dB TDD Tx Power would increase overall device power consumption 7-12%, assuming 100% UL TTI usage, which is absolute worse case.
  Increased use of TDD with higher power will allow device power savings for the offered UL traffic due to frame configuration, compared to continuous FDD transmissions.
  Therefore, use of higher TDD Tx power may have insignificant impact on overall device power consumption.

## Slide 6: 3GPP Power Class Definitions
Currently, nearly all LTE UEs use the same Power Class 3 (+23 dBm)
  Other cellular technologies have multiple UE classes for different purposes.
    GSM/Edge have 5/7 Power Classes, with Tx powers ranging from +23..+39 dBm
    UMTS has 5 Power Classes, with Tx powers ranging from +21..+33 dBm
  3GPP LTE standards designed for 4 Power Classes from the beginning, but to date, full standards definition only complete for Power Class 3.
    One exception: Power Class 1 (31 dBm) for Band 14 introduced in Rel-11
    Power Class 3 was originally defined to maintain cell site count parity with UMTS, which is not applicable to Band 41 deployments.