## Slide 1: Way forward for 3DL/2UL support
Vodafone, []
TSG-RAN Working Group 4 (Radio) meeting #75 R4-153814
Fukuoka, Japan May 25th – 29th, 2015

## Slide 2: Background
For a UE supporting 3DL and 2UL in A, B, C bands it is questionable which of the three 2UL CA pairs shall be supported or not
It is the view of some companies that a UE that supports 3DL/2UL CA among 3 bands/CC should be able to use obviously the 3 bands/CC in DL, and any pair of of the three 2UL. Other than that there will be significant fragmentation in the support of 2UL, and risk for network congestion and lack of deployment flexibility with regards to UL CA planning
It is also the view of other companies that it can add complexity to the UE to support the three 2UL CA pairs under some conditions, e.g. possible duplication of PA, additional components needed to handle specific combinations that need MSD, etc.

## Slide 3: Discussion
For 3DL/2UL CA and a UE that supports LL’H or LHH’
If the UE supported one of the Low+High (e.g. LH) in ULCA
  then the other Low+High (i.e. L’H or LH’) can easily be supported in the terminal since there is no additional complexity (e.g.no need for additional PAs) in the terminal
  Option 1: The remaining L+L or H+H (i.e. LL’ or HH’) support is optional
  Option 2: The remaining L+L or H+H (i.e. LL’ or HH’) support is FFS
If the UE supported LL’ or HH’ in UL CA
  then each low or each high band has its own PA already, so that the UE can easily support the remaining 2 other Low+High combinations (LH and L’H for LL’H terminal, and LH and LH’ for LHH’ terminal)
Thus it can be seen that regardless of what initial 2UL combo is supported in terminal (bullet 3 or 4), Low+High combinations are always supported in the end. It cannot be concluded the same for Low+Low and High+High
MSD discussions are on-going, so support may depend on the outcome, and applicability for new combinations. No discussions on already specified combinations.

## Slide 4: Agreement
For 3DL/2UL CA UE that supports LL’H or LHH’
All Low+High 2UL CA combinations shall be supported
  i.e. LH and L’H in UL for LL’H terminal and LH and LH’ in UL for LHH’ terminal
Low+Low and High+High combinations support is optional
If UE supports Low+Low or High+High combinations in UL, then UE shall support Low+High combinations
The above applies for 2UL combinations already specified, with and without MSD, and for future combinations with no MSD
Due to ongoing discussion on MSD calculation procedure: For new 3DL/2UL combinations with MSD values, the support is FFS
Agreement is to capture this in the specification. TBC how to do it. Aim August meeting to introduce in the spec