## Slide 1: WF for NAICS CQI robustness test
Agenda: 6.6.2
Source: Ericsson
3GPP TSG-RAN WG4 Meeting #75 R4-153848
Fukuoka, Japan, 25th – 29th May 2015

## Slide 2: Purpose
The purpose here is to down select the options presented here to define the CQI robustness test case for NAICS for inclusion into TS36.101

## Slide 3: Online agreements
Agreed Proposal 4: Specify at least one NAICS test for CQI reporting.
Agreed Proposal 4a: Test purpose: CQI robustness for NAICS to ensure CQI reporting not worse than MMSE-IRC CQI reporting under non-NAICS favorable condition assuming NAICS receiver is used for demodulation.

## Slide 4: Evening adhoc agreements
For the parameters specified in Table 9.8.5.1.1-1, and using the downlink physical channels specified in Annex C, the minimum requirements are specified in Table 9.8.5.1.1-2 and by the following
  a)the ratio of throughput with NAICS assistance information obtained when transmitting the transport format indicated by each reported wideband CQI index subject to interference sources with specified and that obtained when the NAICS assistance information is not sent to the UE when transmitting the transport format indicated by each reported wideband CQI index shall be ≥ g ;
Agree in concept (actual wording TBD) the wording above.
Need to further discuss the wideband CQI and the actual gamma value.

## Slide 5: Proposed test scenario - general
CSI reporting setup
  CQI: Wideband reported CQI should be kept for follow CQI.
  RI: fixed RI=1 on serving cell
  PMI:
    Option 1: fixed PMI
    Option 2: follow PMI
SINR levels to be simulated [-6:2:10]
  SINR is used for evaluation purpose in order to pick up a proper test point with reasonable SINR. SNR could be used further for setting up requirement transformed from SINR.
EPA5 on all cells
HARQ retransmission is switched off
All the cells are time synchronous and with no frequency offsets applied

## Slide 6: TM list with test configuration
TM4/4/4 for CRS-based TM with non-colliding CRS, 2x2
TM9/9/9 for DM-RS based TM with non-colliding CRS, 2x2
  Non-overlapping CSI-RS are configured
TM10/9/9 for TM10 with non-colliding CRS, one CSI process, non-overlapping CSI-RS and one CSI-IM, 2x2
    Non-overlapping CSI-RS are configured

## Slide 7: Interference Model
  Low INRs with 2 interfering cells.
  Model types
    Option 1: Fixed interference model.
      Full load with 100% PDSCH scheduled in interfering cells
      Fixed interference using
        Option 1a 16QAM, rank 1
        Option 1b 64QAM, rank 2
      Fixed interferer precoding
    Option 2: Randomized interference model used for the demodulation test cases

## Slide 8: TP with follow CQI to be evaluated
TP curves with follow CQI to be provided as following
  TP1-1: NAICS signaling is configured with NAICS receiver on demod + NAICS receiver on CQI (Note 1)
  TP1-2: NAICS signaling is configured with NAICS receiver on demod + NAICS receiver (up to UE implementation) on CQI with fallback mode switched off
  TP2-1: NAICS signaling is configured with NAICS receiver on demod + MMSE-IRC receiver on CQI (Note 1)
  TP2-2: NAICS signaling is configured with NAICS receiver on demod + MMSE-IRC receiver on CQI with fallback mode switched off
  TP3: NAICS signaling is not configured with MMSE-IRC receiver on both demod and CQI (up to UE implementation to perform pure blind detection to get better performance or not)
Note 1: Up to UE implementation

## Slide 9: Relative throughput ratio
Relative throughput ratio are used
  Gamma1-1=TP1-1/TP3
  Gamma1-2=TP1-2/TP3
  Gamma2-1=TP2-1/TP3
  Gamma2-2=TP2-2/TP3
Notes:
  The minimum results to be provided are TP1-1, TP3 and Gamma1-1 which could be used for alignment purpose and requirement setup.
  The other TPs and Gammas are only for information as a configured setup in order to provide a reference and subject to each company’s wish to provide or not.

## Slide 10: Agreements
RAN4 agrees to further evaluate the test scenarios proposed in the WF and companies are encouraged to bring simulation results for alignment purpose in order to set up requirement for CQI robustness.