## Slide 1: WF on CRS-IM PDSCH demodulation
Ericsson, […]
R4-153850
3GPP TSG-RAN WG4 Meeting #75
Fukuoka, Japan, May 25~May 29, 2015

## Slide 2: Serving cell MCS for non-TM10
For the gain test
  MCS = [18 or16 or 14]
Companies are encouraged to provide simulation results for these MCS. MCS will be decided in the next meeting.
For the robustness test if introduced
  MCS is FFS.

## Slide 3: Test cases for non-TM10
Test cases for the non-TM10 gain test
  TM9/TM9/TM9
  At least one CRS-based transmission mode among the following TMs:
    TM2/TM3/TM3
    TM3/TM3/TM3
    TM4/TM4/TM4
Test cases for the robustness test if introduced
  TM3/TM3/TM3
  Note: The corresponding interference model is referred to clause B.5 of 36.101.
  Apply EVA5 low correlation channel to both serving and interference cells.

## Slide 4: Test setup for TM10
PDSCH scheduling
  Option 1: PDSCH is static scheduled from non-serving TP within CoMP set
  Option 2: DPS, i.e., TP for PDSCH transmission is dynamically changed between two TPs within CoMP set
Interference modelling for the TP within the CoMP set
  Option 1: blanking
  Option 2: Partial load with fixed RU
Interference modelling for the TP outside the CoMP set
  Partial load with lower RU (i.e., 20% or 10%)
Transmission mode for the TPs
  Option 1: TM10/TM10/TM10
  Option 2: TM10/TM10/TM9
  Note: TP1, 2 is within COMP set and TP3 is outside COMP set

## Slide 5: Test setup for TM10
The minimum requirements shall be based on 2-cell generic CRS-IC
The inference profile shall be decided conditioned on:
  All the aggressor cells are detectable
  FFS: Minimum adjustment to the homogeneous network interference profile. It can be used to differentiate 2-cell CRS-IC and 1-cell CRS-IC
    Method for differentiation is FFS.

## Slide 6: Signaling and capability issue
FFS : Companies are encouraged to study the following issues:
  Whether “CRS-AssistanceInfo” is required as the assistance information to trigger CRS-IM receiver?
  Whether and how to extend the CRS-IM receiver to Scell?
  Whether to define capability signaling for CRS-IM feature
  In case, RAN4 agrees on the need for capability signaling for CRS-IM
    How to define capability signaling
    How to handle different UE capability with crs-InterfHandl-r11 or naics-Capability-List-r12?
    How to handle CRS-IC capability for CA?
There is no CA test case for CRS-IC.