## Slide 1: Wayforward on SSTD reporting for DC enhancement
Intel, ….
R4-155613
3GPP TSG-RAN WG4 #76bis
Sophia Antipolis, France, 12 – 16 Oct, 2015
Agenda Item: 7.9.4.1

## Slide 2: Observations
Observation 1: Although SFN/subframe offset in DC enhancement in Rel13 can be used for other usage possibly, it is reasonable to assume UE reporting on SFN/subframe offset between MeNB and SeNB are mainly for
  DRX or measurement gap configuration alignment
  Power control mode selection
Observation 2: It is possible that with UE reporting on the subframe offset between MeNB and SeNB in DC enhancement in Rel13 the error of the sync/async DC deployment decision will be occurred.
Observation 3: When eNB is ambiguous on the sync/async DC deployment from the subframe timing offset via UE reporting, the finer reporting resolution is needed to improve the exact sync/async DC decision. Otherwise, the definite sync/async state can be reported to eNB.

## Slide 3: Wayforward
Proposal 1: The various reporting granularity can be applied for UE reporting on subframe offset between MeNB and SeNB.
Proposal 2: The reporting range for subframe offset between MeNB and SeNB can be specified as:
Reported value | Measured quantity value | Unit
Subframe_TIME_DIFFERENCE_0000 | abs(Z)< 33us-24Ts | Ts
Subframe_TIME_DIFFERENCE_0001 | 33us-24*Ts abs(Z) < 33us-22*Ts | Ts
Subframe_TIME_DIFFERENCE_0002 | 33us-22*Ts abs(Z) < 33us-20*Ts | Ts
… | … | …
Subframe_TIME_DIFFERENCE_0013 | 33us < abs(Z) < 33us+2*Ts | Ts
Subframe_TIME_DIFFERENCE_0014 | 33us+2* Ts < abs(Z) < 33us+4*Ts | Ts
… | … | …
Subframe_TIME_DIFFERENCE_0025 | 33us+22* Ts < abs(Z) < 33us+24*Ts | Ts
Subframe_TIME_DIFFERENCE_0026 | 33us+40* Ts < abs(Z) | Ts
Table 9.x.x.x: UE Subframe offset measurement report mapping