## Slide 1: Wayforward on RRM in LAA
Intel, ….
R4-155616
3GPP TSG-RAN WG4 #76bis
Sophia Antipolis, France, 12 – 16 Oct, 2015
Agenda Item: 7.13.4.

## Slide 2: Wayforward(1)
Upon the latest RAN1 agreements on DRS for LAA RRM measurements, we can propose:
Proposal 1: The requirements for RRM measurement (e.g. cell identification) in LAA can be specified by “X DMTC_period “ assuming one successful DRS transmission within a DMTC period can be guaranteed.
Proposal 2: The measurement accuracy requirements for LAA including the measurement bandwidth need to be further evaluated based on the finalized DRS design.

## Slide 3: Wayforward(2)
Additionally for RSSI measurement in LAA, we propose:
Proposal 1: The definition of LAA RSSI in Rel13 shall be clarified by RAN1 in order to differentiate with the legacy RSSI in [5].
Proposal 2: RRM requirements on the measurement accuracy need to be specified for both average RSSI over averaging granularity and the percentage of time that average RSSI above CCA threshold.
Proposal 3: The requirements on RSSI measurements for both UE and eNB in LAA shall be considered in RAN4.
Proposal 4: The requirements on the RSSI measurement delay in LAA shall be studied.
Proposal 5: The requirements on the interruption due the RSSI measurement gap in LAA shall be specified.