## Slide 1: Way Forward on MSD for CA_28A-42A
KDDI Corporation
3GPP TSG-RAN WG4 #76-bis
Sophia Antipolis, France, 12 – 16 October, 2015
Agenda Item: 7.43.2.2
Document for: Approval
R4-155839

## Slide 2: Background
CA_28A-42A is classified as Class A2 because 5th harmonic of Band 28 UL will fall into Band 42 DL.
Thus, MSD requirements would be needed.
Also for delta values, RAN4 does not have same understanding. So way forward is needed.

## Slide 3: Way Forward
MSD
  Continue studies and conclude in RAN4#77.
Delta values
  Below values should be approved.
  ΔRIB should not be 0 dB because at least there are two relaxation factors. 1) triplexer and 2) HTF.
Inter-band CA Configuration | E-UTRA Band | ΔTIB,c [dB] | ΔRIB [dB]
CA_28A-42A | 28 | 0.5 | 0.2
 | 42 | 0.8 | 0.5

## Slide 4: MTK (R4-155973)
 | H5 (dBm) |  | MSD (dB) |  |  | 
 | Main | Diversity | 5 MHz | 10 MHz | 15 MHz | 20 MHz
w/i harmonic filter | -87.3 | -87.8 | 9.0 | 6.5 | 5.2 | 4.4
Below MSD would be expected.
ANT ISO does not affect MSD improvement so much.

## Slide 5: QC (R4-156520)
No MSD if 1MHz GB is assumed from direct 5th wave.
B42 CH BW | Sensitivity (dBm) | MSD (dBm)
5 MHz | -99.0 | 0.0
10 MHz | -96.0 | 0.0
15 MHz | -94.2 | 0.0
20 MHz | -93.0 | 0.0
Below MSD was observed for direct 5th wave.
B42 CH BW | Sensitivity (dBm) | MSD (dBm)
5 MHz | -82.4 | 16.6
10 MHz | -82.3 | 13.7
15 MHz | -82.2 | 12.0
20 MHz | -82.1 | 10.9

## Slide 6: Delta values
Inter-band CA Configuration | E-UTRA Band | ΔTIB,c [dB] | ΔRIB [dB]
CA_28A-42A | 28 | 0.6 | 0.2
 | 42 | 0.8 | 0.5
KDDI: R4-155838
Qualcomm: R4-155838
Band | Triplexer Loss | HTF filter | Total loss | Del_T_IB | Del_R_IB
B28 | 0.4 | 0.6 | 1.0 | [0.5] | [0.5]
B42 | 1.3 | 0 | 1.3 | [0.8] | [0.5]
TeliaSonera: On-line comment
  ΔRIB for Band 28 should be 0 dB.