## Slide 1: PCell Mandatory Support for several combinations
KDDI Corporation
3GPP TSG-RAN WG4 #76-bis
Sophia Antipolice, France, 12 – 16 October, 2015
Agenda Item: 5.1.4
Document for: Approval
R4-155858

## Slide 2: Contents
[Background] Why we need PCell Support as many bands as possible.
[Analysis] Two specific cases are analyzed.
[Proposals] Several Proposals on Class A2 combinations

## Slide 3: Background
Several companies have made a question “Why UE has to support PCell in all bands?”
We have explained several times by the online comment but it seems one of our main concerns was not still shared in RAN4.
CA_26A-41A is taken as an example to explain.

## Slide 4
Case#1:
If UE supports CA_26A-41A PCell only in B26

## Slide 5
Case#2:
If UE supports CA_26A-41A PCell in both bands

## Slide 6: Analysis for Case#1
In case#1, namely PCell only supported in B26, RAN4 can find two observation.
  Observation#1: When B26 UL resource is full, new UE in B26 only area cannot be accepted unless B26 UL resource becomes available.
  Observation#2: In order to accept new UE in B26 only area, CA_26A-41A configuration is changed into B26 single operation. This user will have an experience on throughput degradation.

## Slide 7: Analysis in Case#2
In Case#2, namely PCell operation is supported in both bands (B26 and B41), RAN4 can also find two observations.
  Observation#1: UL resources can be balanced.
  Observation#2: Changing CA_26A-41A configuration into single B26 is not needed not likely in Case#1. This reduces the number of signaling and avoids throughput degradation.

## Slide 8: Proposals
We propose PCell configurations as below.
CA Configuration | PCell Support Mandatory | PCell Support Optional | Comments
CA_1A-28A | Band 1 Band 28 (~R12) | Band 28 (R13~) | Up to Rel-12, PCell support in B28 should be mandatory to avoid UE fragmentation. From Rel-13 onwards, PCell support in B28 will be decided by capability signaling.
CA_26A-41A, CA_26A-41C | Band 26 Band 41 |  | 1) PCell support in B41 depends on how to handle harmonic mixing issue. 2) This is Class A2 combination but HTF is not assumed so B26 can always become PCell.
CA_1A-42A, CA_1A-42C | Band 1 | Band 42 |