## Slide 1: Way Forward on inter-frequency/inter-PLMN Discovery
Ericsson, Qualcomm, Nokia Networks, Intel Corporation
R4-156633
3GPP TSG RAN WG4 Meeting #76bis
Sophia-Antipolis, France, October 12-16

## Slide 2: Background
Gaps for inter-frequency/inter-PLMN discovery
  Gaps also applicable to intra-frequency discovery
  As RAN2 is currently discussing the details on gap definition, RAN4 could not reach any consensus related to gaps.
Transmission timing requirements [RAN1 Chairman notes]
  “When a UE transmits D2D discovery in non-primary carrier:
    If the UE has the activated serving cell in non-primary carrier, then the activated serving cell is always used for DL measurements and synchronization
    Otherwise, one single DL carrier is used for DL measurements and synchronization for a given SL transmission.
      This single DL carrier is signaled (details left to RAN2)”

## Slide 3: Way Forward
When discovery Tx is on non-Pcell, the existing transmission timing requirements (section 7.16.2.1) can be reused w.r.t. the following timing references
  When discovery Tx is on activated SCell, then Scell DL timing is used as reference.
  Otherwise, the DL timing of the associated cell used for discovery synchronization as reference.
    The DL carrier frequency to be used for discovery synchronization is signaled by the serving eNodeB. Associated cell is selected as per RAN2 procedures.
RAN4 shall further discuss on interruptions and gaps for D2D discovery and communication operation on inter-frequency/inter-PLMN at next RAN4#77 meeting.