## Slide 1: WF on Discovery RSRP measurement accuracy
Qualcomm Incorporated, Ericsson, Nokia Networks
R4-156634
3GPP TSG-RAN WG4 Meeting #76bis
Sophia Antipolis, France, Oct. 12th – Oct. 16th, 2015

## Slide 2: Background
In RAN4#76, simulation assumptions for Sidelink Discovery RSRP (SD-RSRP) measurement accuracy were agreed in R4-155193
Two scenarios were agreed
  Scenario 1: without colliding PSDCH
  Scenario 2: with colliding PSDCH

## Slide 3: Proposals
Proposal 1: Companies encouraged to provide results for both colliding and non-colliding PSDCH case
  RAN4 has not yet concluded on whether SD-RSRP requirements are to be defined for colliding PSDCH case or for non-colliding PSDCH case
  Down-selection can be made in RAN4#77 for the purpose of defining the requirements
Proposal 2: Specify requirements only for numRetx = 3
  Time separation between two retransmissions
    AWGN (for simulations and requirements): N/A
    Fading (for simulations)
      0ms (subsequent subframes)
      Optionally companies can provide results for 4ms, 8ms, 20ms
  The SD-RSRP accuracy shall be met over L1 measurement period (T1); PSDCH transmission and retransmissions are assumed to be transmitted within T1.
Proposal 3: Assume soft-combining to define SD-RSRP accuracy requirements
  Note these measurements are applicable to UEs that support both discovery and communications
  Assuming non-concurrent WAN / D2D communication operation
  Does not mandate soft-combining for legacy discovery (not related to Relay discovery)
  Does not mandate any UE implementation
Proposal 4: Use existing RSRP/S-RSRP accuracy requirements with minimum SINR is derived based on (Impairment results + Margin) for PSDCH demodulation s.t.,
  Legacy RSRP/S-RSRP measurement accuracy requirements are met
  PSDCH BLER is < 0.01%
  Companies are encouraged to provide impairment results in the next meeting based on simulation assumptions in R4-155193