## Slide 1: Way Forward on eMTC measurement requirements
Ericsson, Nokia Networks
R4-156657
3GPP TSG RAN WG4 Meeting #76bis
Sophia-Antipolis, France, October 12-16

## Slide 2: Background
RAN4 has studied measurement performance for Rel-13 MTC for the last few meetings.
This has resulted in following 3 outgoing LS responses:
  R4-155112, “LS response on measurement performance for Rel-13-MTC”
  R4-155113, “Reply LS on PRACH coverage enhancement for eMTC”
  R4-155119, “LS reply on measurements cell selection and reselection for MTC LC/EC”

## Slide 3: Proposals for normal coverage
RAN4 shall focus on defining intra-frequency RRM requirements for Rel-13 MTC UEs under:
  Normal coverage
  Enhanced coverage
RAN4 is open to define inter-frequency RRM requirements.
For normal coverage:
  Rel-12 category 0 RSRP/RSRQ measurement accuracy requirements are reused.
  RSRP/RSRQ L1 measurement period may be longer than that defined for category 0 due retuning.
  Cell identification delay may be longer than that defined for category 0 due to retuning.
  New RLM requirements are defined due to the new control channel (e.g M-PDCCH).
  New SI reading requirements are defined.
  IDLE mode requirements for Rel-13 normal coverage UEs are defined based on corresponding CONNECTED mode requirements in longer DRX i.e. same measurement period in idle mode and connected for same DRX cycle length.

## Slide 4: Proposal for enhanced coverage
For enhanced coverage:
  Rel-12 category 0 absolute RSRP requirements is reused down to -12 dB SNR for AWGN.
  For SNR levels <-12 dB down to FFS, absolute RSRP accuracy is relaxed by 1.0 dB for baseband (i.e. +/- 8dB requirement) for AWGN.
  Rel-12 category 0 relative RSRP requirements is reused down to -12 dB SNR.
  For SNR levels <-12 dB down to FFS, relative RSRP accuracy is relaxed by 1.0 dB (i.e. +/-5dB requirement) for AWGN.
  L1 measurement performed is extended from legacy 400 ms for Rel-12 category 0 requirements.
  New cell search requirements are defined.
    Interested companies are encouraged to provide simulation results according to assumptions in R4-156656.
  New RLM requirements are defined due to new control channel (e.g. M-PDCCH).
  New SI reading requirements are defined.
  IDLE mode requirements for Rel-13 enhanced coverage UEs are defined based on corresponding CONNECTED mode requirements i.e. same measurement period in idle mode and connected mode for the DRX cycle length under same SNR range.
  Note: For fading scenarios the estimation techniques used in RRM measurement demonstrates worse performance than under AWGN conditions as noted in [R4-155112].