## Slide 1: WF on EIRP value
NTT DOCOMO,INC., [KATHREIN], [Telecom Italia]
3GPP TSG-RAN WG4 Meeting #76-bis R4-156819
Sophia Antipolis, France, 12 – 16 Oct, 2015 Agenda 7.2.3.2

## Slide 2: Background
EIRP accuracy value has been discussed in several meetings.
Up to now it was not possible to converge on a value.
In this contribution, WF on how to decide one accuracy value in RAN4#77 is presented in following slides.

## Slide 3: WF(1/2)
  Proposed values up to RAN4#76 are described in slide 5.
  In RAN4#77, RAN4 decide the accuracy value by using either four options below;
    Derive by averaging all of proposed values
      Averaged each error sources (Transceiveraccuracy, steeringerror and arrayerror) value, or averaged each proposed values.
    Derive as Root sum square of three error sources averaged values other than Ericsson’s. And weighted (8:1) the obtained value and Ericsson's one.
    Transceiver accuracy is set as 2dB according to conducted output power accuracy. Other two error sources (steeringerror and arrayerror) is obtained by averaging all of proposed values from companies. Derive accuracy value as Root sum square of above the three values.
    Any other options (proposed in RAN4#77) of how to calculate accuracy value by using values shown in slide 5.

## Slide 4: WF(2/2)
  In RAN4#77, companies submit contributions of which option shown in slide 3 should be applied.

## Slide 5: [Info]proposed values
Proposed values by companies
 | 3 error model (AAS performance) |  |  |  | Proposal
 | Transceiver accuracy | Steering error | Array error | total (3err) | 
CATT (Checked) R4-145627 | 2 (2.5) | 0.5 (1) | 1.2 (1.7) | 2.2 (3.2) | 2.4
NEC (Checked) R4-145901 | 2 | 1.5 | 1.5 | 2.9 | 2.9
Huawei(Checked) R4-146176 | 2 | 0.5 | 1 | 2.3 | 2.3
Ericsson R4-146289 | 1 to 2 | 0.5 | 0.5 to 1.5 | 1.5 to 2.8 | 2.25
Nokia Networks(Checked) R4-150960, R4-153498 | 2 | 1.5 | 1.5 | 2.9 | 2.9
Vodafone(Checked) R4-75AH-AAS-0087 | 1 | 0.5 | 1 | 1.5 | 1.5
Telecom Italia R4-146708, R4-146104 | 1 | 0.5 | 1 | 1.5 | 1.5
CMCC(Checked) R4-75AH-AAS-0005 | 1 | 0.5 | 1 | 1.5 | 1.5
Katrein(Checked) R4-152625 | 1 | 0.5 | 1 | 1.5 | 1.5
Note：data in ”()” denotes extreme condition.
Note：red color with yellow highlighted denotes under checking