## Slide 1: NB-IOT in-band operation: Co-existence study
Nokia Networks
R4-157926
3GPP TSG-RAN WG4 #77
Anaheim, CA, US, 16 – 20 Nov, 2015
Agenda Item: 7.50.3
Document for information

## Slide 2: References
GERAN TR 45.820
TR 36.942
TR 25.942
[1] RP-151621, “New Work Item: NarrowBand IOT (NB-IOT)”, Qualcomm
[2] R4-156755, “Way Forward on Simulation Assumptions and Methodology for NB-IOT coexistence study”, Nokia Networks, Ericsson, ZTE

## Slide 3: NB-IOT in-band operation: background
In-band operation
  NB-IOT is operating inside LTE system bandwidth
  1PRB is reserved for NB-IOT
Two DL approaches
  15kHz subcarrier spacing
  3.75kHz subcarrier spacing

## Slide 4: NB-IOT in-band operation: co-existence study
Co-existence study shall be used to evaluate mutual interference between LTE and NB-IOT for in-band operation.
Static system level simulation, as used for RAN4 co-existence study, shall be used to evaluate interference impact.
There are two DL NB-IOT proposals for in-band operation
  15kHz subcarrier spacing: No need for co-existence study, because the in-band NB-IOT PRB is orthogonal to LTE PRBs.
  3.75kHz subcarrier spacing: Need to study co-existence impact, because the NB-IOT PRB is no longer orthogonal to LTE PRBs.
This contribution provides simulation results for DL co-existence study.

## Slide 5: Evaluation methodology
The co-existence study methodology follows TR 36.942, and simulation assumption contribution R4-156755
Static system simulation
  ACLR is reused at PRB level.
NB-IOT to LTE interference
  Adjacent PRB interference, specified with ACLR at PRB level.
LTE to NB-IOT interference
  Adjacent PRB interference, specified with ACLR at PRB level.
  In-band interference due to CRS
Other relevant parameters to follow RAN1 agreements captured in R1- 156284
Metrics:
  For NB-IOT use SINR
  For LTE use SINR and throughput loss (based on SINR to throughput mapping in 36.942)

## Slide 6: Simulation Assumptions
Parameter | Value | 
Frequncy | 2GHz | 
LTE system bandwidth | 10 MHz | 
Network layout | Wrap around 57 sectors (figure 4.2 in TR 36.942) | 
Base station total TX power | 46 dBm, shared by all LTE PRBs and NB-IoT | 
NB-IOT Power boosting | 6dB | 
LTE PRB index for NB-IOT transmission | 10 | 
UE max transmit power | 23dBm | 
NB-IOT UE max transmit power | 23dBm | 
ACS | LTE: 33dB; NB-IOT: 35dB | 
DL power control | N/A | 
UL power control | based on sub-clause 5.1.1.6 of 3GPP TR 36.942 | 
UE antenna gain | 0dBi | 
Penetration loss | Based on Annex D.1 of TR 45.820 (No additional building penetration loss for the NB-IoT as aggressor) | 

## Slide 7: Interference model
NB-IOTLTE (victim) interference
  Adjacent PRB interference is dominant. The adjacent PRB interference is evaluated with ACLR at 180kHz (1PRB) offset.
LTE  NB-IOT (victim)
  Adjacent PRB interference is evaluated with ACLR.
  In-band interference due to CRS interference is modeled as an extra interference for capacity loss.

## Slide 8: LTE  NB-IOT (victim): CRS interference model
For 3.75kHz subcarrier spacing, CRS RE puncturing is assumed for NB-IOT UE.
About 1/3 of NB-IOT RE will be punctured due to LTE CRS RE.
  There will be 67% reduction of throughput.
  Higher SINR is needed to reach the same level of throughput.
  At the same throughput level, the loss of SINR is considered as the impact of CRS interference.

## Slide 9: CRS interference model
Use Shannon equation to model the loss of SINR.
, where is the SINR, as the loss of throughput, and is defined as the loss of SINR.

## Slide 10: Performance evaluation
Performance evaluation shall be based on TR 36.942 and [2]. The degradation of SINR and LTE throughput shall be presented as a function of ACIR
  ACIR is evaluated based on

## Slide 11: ACLR and Typical ACIR values
ACLR shall be based on single PRB to evaluate NB-IOT impact
  ACLR = Mean power of 1 PRB / mean power of neighbor PRB
NB-IOT (3.75kHz)  LTE (victim)
  Use GSM Tx SEM: ACLR1 = 29dB.
  Use LTE ACS=33dB.  ACIR = 27.5dB
LTE  NB-IOT (victim)
  Typical LTE ACLR (45dB) is base on full LTE bandwidth (1.4MHz and beyond) (36.104).
  There is no specified LTE ACLR and LTE SEM at single PRB level.
   It is not clear about the typical ACIR value.

## Slide 12: NB-IOT (3.75kHz spacing)  LTE
A suitable NB-IOT filter with a large ACLR will ensure small impact to LTE system.
Typical ACIR=27.5dB
Typical ACIR=27.5dB

## Slide 13: LTE  NB-IOT (3.75kHz spacing)
Dominant interference to NB-IOT is the CRS interference. The interference is in-band interference, independent from ACLR
The SINR degradation for average NB-IOT UE is >3dB; for cell edge UE, the degradation >1.7dB.

## Slide 14: Observations
DL co-existence simulation results are provided for in-band operations with the 3.75kHz subcarrier design.
For NB-IOT  LTE (victim)
  LTE throughput loss is relatively small for 10MHz BW LTE.
For LTE  NB-IOT (victim)
  Dominant interference to NB-IOT is observed. The interference is in-band interference, independent from ACLR
  The SINR degradation for average NB-IOT UE is >3dB; for cell edge UE, the SINR degradation >1.7dB.