## Slide 1
3GPP TSG-RAN WG4 #77 R4-158064
November 16th ‒ 20th, 2015
Anaheim, US
Agenda item: 7.45
Document for: Discussion
Potential solutions for antenna isolation
Qualcomm Incorporated

## Slide 2: Discussion points
Key objectives irrespective of the actual value of antenna isolation to be assumed
A specification from which expected radiated performance can easily be derived (i.e., just by adding a fixed antenna gain)
  Radiated testing can be a solution here, but some disadvantage (see #2)
  Does this need to be tested or is guidance enough? Testing is beneficial to validate the implementation without having to rely on an antenna system.
    However, without an antenna system, the validation is not entirely precise since it is against a specification that had an antenna isolation assumption built in
A specification that allows the chipset and handset to be validated independently of the antenna system (since the antenna design may come much later and from separate entity)
  Implies that radiated testing alone would not be a workable solution. Will always need some sort of conducted test instead of or in addition to radiated.
  Does this include verification of the phone design sans antenna? i.e., including PCB coupling, etc? Is that a meaningful objective? For whom?
Alignment of test procedure to core requirement (vice versa doesn’t make sense)
  Appears to be a RAN5 discussion, but perhaps with guidance from RAN4
  Recognize that there are often very good reasons why test procedure and core requirement are not always the same (usually test time and complexity), but again, this is RAN5 judgment
Reduce refsens, MSD margins in specification
  Is this really an objective, or is it a byproduct? If this is truly an objective, I recommend it be taken on in a broader context by its proponents.

## Slide 3: Potential solutions (none of which are perfect)
Conducted testing solutions
  Revise the core specifications to include antenna port isolation assumption that is built on isolation available without the antenna system (i.e., PCB)
    This would enable validation of the platform without antenna system
    This would not provide a good estimate of fielded performance with an antenna
      Therefore, this test might be more useful to chipset vendor and maybe handset vendor, but would not be meaningful to an operator. Perhaps not appropriate as a 3GPP requirement.
Two specs
  One spec to address the conducted aspect and a second aspect to address the radiated aspect, either directly or indirectly
    In general, it is not advisable to have two specs for the same thing
    Have we doubled the work? What have we gained? Will devices work better now as a result? Or have we simply created more work for little to no benefit?
Remove testing of some specs
  For those specs that are highly dependent on antenna isolation (MSD, harmonic), the testing is of limited value, especially if the MSD is very high
Retain the status quo