## Slide 1: WF on RRM requirement for UE-NW relays
Qualcomm Incorporated, Nokia Networks, Intel Corporation, LG Electronics
R4-158143
3GPP TSG-RAN WG4 Meeting #77
Anaheim, CA, Nov 16th – Nov 20th, 2015

## Slide 2: Background
In Rel-13 eD2D, RAN4 needs to defined the following requirements for UE-NW relays
  SD-RSRP measurement accuracy requirement
  Relay selection / reselection
Alignment results for minimum SNR for defining the SD-RSRP accuracy requirements
  Simulation assumptions: R4-155193 and R4-156634
  Non-colliding; AWGN
Company | Minimum SNR (dB) (impairment results)
Intel | -2.8
LGE | -2
Qualcomm | -1.7
Ericsson | -3
Average + Margin ([0.8]dB) | [-1.5]

## Slide 3: Proposals on SD-RSRP
Proposal 1: SD-RSRP accuracy requirements are defined for AWGN and non-colliding PSDCH scenario
Proposal 2: For SD-RSRP accuracy requirements, legacy RSRP accuracy requirements are reused with the following changes:
  SNR instead of SINR
  Minimum SNR at which the requirement can be met is [-1.5dB]
  Applicable to both absolute and relative accuracy requirements
  FFS on if and how to capture time separation of retransmissions when specifying the requirements
Proposal 3: RAN4 shall resolve the FFS in RAN4#78

## Slide 4: Proposals on relay selection/reselection
Proposal 3: RAN4 to define Tmeasure and Tevaluate for relay selection/reselection
  Assuming the connected relay UE and other candidate relay UEs are transmitting every discovery period