## Slide 1
3GPP TSG-RAN WG4 Meeting #80bis R4-168508
Ljubljana, Slovenia, 10 - 14 Oct, 2016
Agenda item: 10.5.2.1
Document for: Approval
UE RF transmitter requirements for below 6GHz
KDDI Corporation

## Slide 2: Background
RAN4 has been quite active to find possible requirements for NR.
Especially for below 6GHz, it seems that some companies prefer to reuse same requirements as LTE for NR.

## Slide 3: Discussion
Most of LTE requirements had been defined Rel-8 era (around 2008).
Considering 8 years have past from Rel-8 initial specification, some requirements might be able to tighten.
In Japan, coexistence between Lower Band 1 and PHS is quite tough (up to 11 dB A-MPR required).
If UE RF transmitter requirements (SEM, MPR, ACLR, etc…) can be tighten even 1 or 2 dB, we can expect lowering A-MPR magnitude for protecting PHS.
As one of example, IQ image above 2GHz was tightened. This implies that there might be other requirements which can be modified.

## Slide 4: Conclusion
For below 6GHz NR UE RF transmitter requirements, it is too fast to decide reusing LTE requirements.
Although we understand time is quite limited to close this SI, it would be beneficial for RAN4 to study possibility whether some requirements can be tightened or not.
It is our expectation that 3GPP NR requirements would be utilized for a long time in the future. Therefore initial core requirements should be defined with special care.