## Slide 1: Way forward on unidirectional RRH arrangement
Ericsson, Vodafone, Telecom Italia, NTT DoCoMo…
3GPP TSG-RAN WG4 #80bis
Ljubljana, Slovenia, 10-14 October, 2016
R4-168663

## Slide 2: The SFN Deployments studied in High Speed Trains
Unidirectional RRH arrangement
With UL RX and DL TX in the same direction the UE experience an almost constant Doppler shift and the base station will experience twice the Doppler on UL RX, but the Doppler will be constant i.e. no sign alternations. This configuration is backward compatible with unmodified Rel-8 terminals.
Bidirectional RRH arrangement
In this case every RRH has antenna lobes for both Rx and Tx in both forward and backward directions. Thereby in the DL , when the UE is in the middle between two RRHs the UE receives two paths with a very big Doppler frequency difference, therefore the UE needs a new advance receiver for this configuration.
f0
f0+870 Hz
f0-870 Hz
f0
f0+870 Hz
f0-870 Hz

## Slide 3: Background
Bidirectional will be specified for 350 km/h at 2.7GHz. At higher speed the performance degrades due to the two paths with very different Doppler shift.
Unidirectional deployment has a good performance at much higher speed since the UE only receives paths with one Doppler shift which will be compensated by the AFC. Thereby unidirectional deployments is not sensitive to high Doppler in DL

## Slide 4: Background (2)
Rationale to introduce test cases for unidirectional deployment
  Shows the LTE system can handle 500km/h
  Shows that the AFC and AGC of the UE can handle the quick changes of frequency and gain due to the directive antennas in the unidirectional deployment

## Slide 5: WF on HST unidirectional deployment
No agreement yet to include unidirectional deployment in the RAN4 specs
In the presented simulations in RAN4 it is shown that the unidirectional deployment supports a High Speed Train going in at least 500km/h.
There is no need for new UE performance tests with the unidirectional deployment since a legacy UE according simulations have a good performance in this scenario.
Way Forward: To introduce the unidirectional deployment scenario with speed 500 km/h in 36.101, e.g. included as an alternative HST scenario in section 8.2.1.1.1, test 4. Then the UE vendors can choose which test to run and thereby there is no impact on the UE testing.