## Slide 1: Way Forward on NB-IoT PRACH performance requirements
Nokia, Ericsson, Samsung, Huawei, ZTE
R4-168745
3GPP TSG-RAN WG4 #80
Ljubljana, SI, 10 - 14 Oct 2016

## Slide 2: Agreements
The SNR for NPRACH minimum performance
  defined based on Missed detection probability <=1%, including: detecting different preamble than the one that was sent, not detecting a preamble at all, or detecting the correct preamble detection but with the wrong timing estimation.
Timing limit :
  7*16Ts=3.646us
Proposals for defining NPRACH performance requirements
  Interested companies are encouraged to
    provide the ideal simulation results as per the simulation assumptions in the following slide, and distribute the results in RAN4 reflector no later than Oct 28;
    provide the practical simulation results and distribute the results in RAN4 reflector no later than Nov.1;
    NPRACH performance requirements will be determined in RAN4#81 based on submitted practical simulation results
    If there are still large difference in practical simulation results from interested companies, additional margin [x dB] may be added into the averaged practical simulation results. The additional margin [x dB] will be determined in RAN4#81.

## Slide 3: Simulation assumptions
Parameter | Values
NPRACH preamble format | 0
Number of Repetitions | 8, 32
Number of Subcarriers | 12
Antenna configuration | 1 x 2
Narrowband physical layer cell identity | 0
NPRACH signature | 0
frequency offset | 0Hz (AWGN); 200Hz EPA1
Propagation channels | AWGN, EPA1
Detection performance | Missed detection rate (1%) with false alarm rate (0.1%)
Timing estimation | Timing error probability with the limit of 3.646us
Timing Offset | [30]us