## Slide 1: Way forward on NPBCH Performance Requirements
Intel, Qualcomm, Samsung, Ericsson, LGE
3GPP TSG-RAN WG4 Meeting #80bis
Ljubljana, Slovenia, 10 - 14 Oct, 2016
R4-168809

## Slide 2: Background
In RAN4 #80, it was identified that Rel-13 NPBCH performance within 1-MIB TTI appeared not enough to achieve the given target SNRs.
RAN1 assumes a NB-IoT UE to try multiple N-MIB TTIs to acquire N-MIB information, accordingly RAN4 investigates the N-MIB acquisition time.
In RAN4 #80bis, RAN4 considers if the acquisition time is introduced as one of NPBCH test conditions to achieve the target SNRs.

## Slide 3: N-MIB Acquisition Time Observations
Based on the study proposals in R4-167085, RAN4 observed the following based on simulation results in RAN4 80bis
    [3~10] TTIs of 640ms are required for N-MIB acquisition with target SNR = -12dB
Test Case | Config | Huawei | E/// | ZTE | QC | CATT | Samsung | Nokia | Intel
1 | EPA-1Hz 1X1 1% BLER | -2.8dB (1TTI) | -4.5dB (1TTI) -10.5dB (10TTI) | -5.1 (1TTI) -9.6 (2TTI) -11.7dB (3TTI) | -7dB (1TTI) -12.1(4TTI) -12.5(5TTI) -13.1(6TTI) | -3.9 (1TTI) -6.8 (2TTI) -8.6 (3TTI) | -3.3dB (1TTI) |  | -4.5 (1TTI) -11.5 (4TTI) -12.4 (5TTI) -13.0 (6TTI)
2 | EPA-1Hz 2X1 1% BLER | -8.1dB (1TTI) -10.7dB (2TTI) -12 dB (3TTI) | -7.5dB (1TTI) -12.1dB (10TTI) | -8.2dB (1TTI) -12.4dB (4TTI) | -8.5 (1TTI) -12.5(4TTI) -12.7(5TTI) -13.1(6TTI) | -5.8 (1TTI) -7.9 (2TTI) -9.7 (3TTI) | -6.1dB (1TTI) | -6.6dB (1TTI) | -8.0 (1TTI) -12.5 (4TTI) -13.0 (5TTI) -13.5 (6TTI)

## Slide 4: WF on NPBCH Performance Requirement
NPBCH BLER target is 1%
NPBCH demod performance requirement should achieve the target SNR (-12dB)
N-MIB acquisition time is taken into account for the NPBCH demod performance requirement at the target SNR.
    The N-MIB acquisition time length, ‘W’, is selected in integer steps of 640ms (see page 3)
    The pm-bch is defined for each NPBCH decoding attempt within ‘W’
    The receiver characteristics of NPBCH for UEs supporting coverage enhancement are determined by the probability of miss-detection of the NPBCH (Pm-bch), which is defined as
      Where A is the number of keep trying intervals with at least one successfully decoded N-MIB PDU and B is the total number of keep trying intervals.
    ‘W’ value is determined based on the results with RF impairments
Companies are encouraged to bring simulation and impairments results for NPBCH to derive the SNR requirements and ‘W’ value in RAN4 #81.