## Slide 1: 3GPP TSG-RAN WG4 Meeting #80Bis Ljubljana, Slovenia, 10-14, October, 2016
Huawei, China Telecom, Nokia, ZTE
Way forward on BS IC
R4-168976

## Slide 2: Background
In RAN#73 meeting, the new study item on interference cancellation receiver for LTE BS was approved in RP-161485

## Slide 3: Scenario
Interference type:
  Intra-cell inter-user interference
  Further discuss on whether to model inter-cell interference in the link level evaluation
Deployment scenario:
  Homogeneous deployment with macro cell only
  Heterogeneous deployment with co-channel low power node(LPN) within the macro cell coverage
  Further discuss if both are to be investigated in the SI
Channel
  PUSCH to PUSCH collision

## Slide 4: Reference Receiver
Reference Receiver
  Option 1: CWIC
    CWIC is used to mitigate uplink intra-cell inter-user interference
    IC iteration may or may not be implemented to further improve the receiver performance
    the Rel-13 BS MMSE-IRC receiver can be applied simultaneously for inter-cell interference suppression while CWIC receiver is used for intra-cell interference cancellation, if inter-cell interference are to be modelled
  Option 2: SLIC
  Down-selection to be made in the next meeting by taking complexity and performance into consideration
Baseline receiver for performance comparison
  MMSE receiver for intra-cell interference scenario only
  Rel-13 BS MMSE-IRC for inter-cell interference suppression, if inter-cell interference are to be modelled

## Slide 5: Intra-cell Interference Model
SNR distribution for the multiple co-scheduled UEs within the target cell
  Option 1: Equal average SNR (short-term variation remains)
  Option 2: Unequal average SNR (e.g., uniformly distributed within a range of [3] dB, and proponents should report their assumption)
  Other options are not precluded

## Slide 6: Inter-cell Interference Model
The following are considered as baseline, if inter-cell interference are to be modelled
Other options are not precluded.
Reuse DIP based interference statistical measurement for BS IC
Reuse the DIP profiles from BS MMSE-IRC WI
FFS number of inter-cell interference
Interference level
  Option 1: cover two interference levels
    high interference level which corresponds to the DIP1 values at 85%-tile of the DIP1 distribution
    low interference levels, which corresponds to 15%-tile of the DIP1 distribution
      For low interference level, if the link performance difference between low interference and AWGN only is negligible, there is no need to model explicit inter-cell interference in the link evaluation.
  Option 2: other options are not precluded
Produce randomly modulated 16QAM symbols in the inter-cell interfering PUSCH.
The boundaries of allocated PRBs for targeting user and interference users are always aligned.

## Slide 7: Link Evaluation Parameters
Performance Metric:
  Option 1: compared the target user throughput between advanced receiver and baseline receiver
  Option 2: compare the sum of throughputs of all the intra-cell users between advanced receiver and baseline receiver
  Other option not precluded
Bandwidth: 10MHz
PRB allocation:
  Option 1: full PRB allocation
  Option 2: 6 PRB in the middle of the channel bandwidth.
UE Tx antenna number: 1
BS Rx antenna number:
  Option 1: 2, 4, 8
  Option 2: 2, 4 as baseline, and FFS on 8

## Slide 8: Open issues (for information)
Companies are invited to provide input on the following open issues:
For intra-cell UEs:
  Number and Spatial correlation level for the multiple co-scheduled UEs within the target cell for BSs with different Rx antennas
    The definition and modeling of different correlation levels need to be discussed
  Number of intra-cell interferers / layers to be cancelled for BSs with different Rx antennas
  MCS for the multiple co-scheduled UEs within the target cell
  Timing delay and frequency offset between co-scheduled UEs
For both intra-cell and inter-cell UEs (if inter-cell interference are to be modelled)
  Propagation condition
  DMRS configuration