## Slide 1: 3GPP TSG-RAN WG4 Meeting #78 St. Julian’s, Malta, 15-19 February 2016
Huawei, HiSilicon
Way forward on demodulation performance and CSI requirements for LAA
R4-160744

## Slide 2: UE demodulation requirements
        Introduce new PDSCH tests in CA mode with at least one licensed CC for LAA DL burst transmission, and the performance on LAA Scell will be verified
  Follow per-CC approach similar as that used for 3DL CA demodulation tests to specify the requirements to make requirements be flexible
  Introduce TM3 tests with PDCCH self-carrier scheduling and TM9 tests with EPDCCH self-carrier scheduling, and for both TM3 and TM9 tests:
    CA bandwidth combinations: 20MHz+20MHz;
    Antenna configurations and correlation matrix: 2x2 Low and 2x4 Low;
    MCS: [16QAM 1/2] for 2x2 case and [64QAM 1/2] for 2x4 case;
    Synchronization: frequency offset and timing error should be set relative to PCell and the practical synchronization algorithm should be considered;
    Burst transmission pattern should be specified;
    Relative throughput as test metric: 70% TP as starting point.

## Slide 3: CSI reporting requirements
        Introduce one CSI reporting requirement to verify the correct UE behavior of CSI measurement averaging for LAA, and for the test there are two options
  Option 1: Define a TM1 1x2/1x4 20MHz(licensed CC)+20MHz(LAA CC) CQI definition test under AWGN with two sets of interference levels and with BLER criterion and CQI distribution with respect to medium CQI as the test metric;
  Option 2: Define a TM1 1x2/1x4 20MHz(licensed CC)+20MHz(LAA CC) CQI definition test with two sets of interference levels and with BLER criterion and the reported CQI distribution only as the test metric
  Other options are not precluded.