## Slide 1: WF on BS RF requirements
Ericsson, [ALU, Huawei, NEC, ]
3GPP TSG-RAN WG4 Meeting #78 R4-xxx
Malta, 15-19 Feb, 2016

## Slide 2: Background
This contribution captures the intial agreements for NB-IOT BS RF requirements which were endorsed in RAN4 NB-IOT Ad-Hoc in Budapest.
It also lists topics that needs further investigation and discussion in next meeting.

## Slide 3: Transmitter requirements agreement
Same BS Types as LTE:
    Wide Area top priority
    Home Area down prioritized
Transmitted signal quality:
    Same as LTE
    DL RS power: tbc with RAN1 outputs
Unwanted emission when in/guard band
    Same as LTE

## Slide 4: Transmitter Requirements (to investigate)
  BS types to consider
    Medium range and local area
  Output power dynamics (in/guard band only)
  Pending on power boosting (+6dB)
ACLR
  Pending on coexistence outcomes
Unwanted emission / Mask
  FFS: GSM or MSR mask for standalone
  when guard band
    FFS: NB-IoT Foffset in LTE guard band
Spurious emission NB-IoT
  Same as LTE

## Slide 5: Transmitter Requirements
RF requirements | LTE + NB-IoT in band / guard band |  | NB-IoT standalone
 | LTE | NB-IoT | 
Base station output power | No change | Power sharing | To specify
Output power dynamics | No change | To specify | To specify
Transmitted signal quality |  |  | 
Modulation quality | No change | Similar LTE | Similar LTE
Frequency error | No change | Similar LTE | Similar LTE
Time alignment error | No change | Similar LTE | Similar LTE
Unwanted emissions |  |  | 
Transmitter spurious emissions | No change |  | To specify
Operating band unwanted emissions | No change To be checked with guard band |  | To specify
Occupied bandwidth | No change To be further clarified with guard band |  | To specify
ACLR | No change | NA | To specify
Transmitter intermodulation | No change | Interferer to be redefined | Interferer to be redefined

## Slide 6: Receiver requirements (to investigate)
NB-IoT REFSENS
  Top priority as it’s used for the other requirements
  Define Fixed Reference Channel
Others
  ACS pending on coexistence.
  Pending on REFSENS.

## Slide 7: Receiver requirements
RF requirements | LTE + NB-IoT in band / guard band |  | NB-IoT standalone
 | LTE | NB-IoT | 
Reference sensitivity level | No change | To specify | To specify
Dynamic range | No change | To specify | To specify
In-band selectivity and blocking |  |  | 
Blocking | No change | To specify | To specify
Narrowband blocking | No change | To specify | To specify
Out-of-band blocking | No change | To specify | To specify
Receiver spurious emissions | No change | No change | No change
Receiver intermodulation |  |  | 
Intermodulation | No change | To specify | To specify
Narrowband intermodulation | No change | To specify | To specify
In-channel selectivity | No change | To specify | To specify
Performance requirements | No change | To specify | To specify