## Slide 1: Way Forward on further work on NB-IoT
Ericsson, CMCC, Intel Corporation
R4-160982
3GPP TSG RAN WG4 Meeting #78
Malta, 15-19 February, 2016
Agenda Item: 3.2

## Slide 2: Proposals on further work on NB-IoT
Measurements and mobility
  RAN4 is to identify the types of signals that are feasible for RRM measurements in RRC_IDLE state.
  RRM measurement performance is to be studied for each deployment type (in-band, guard-band, stand-alone) independently and the corresponding requirements shall be defined accordingly for NB-IoT UEs in RRC_IDLE state.
  RAN4 is to analyse the impact of deployment type on the cell reselection procedure/requirements for NB-IoT UEs in RRC_IDLE state.
  Measurement accuracy is to be considered for RRM measurements in RRC_IDLE state
  RAN4 will not define measurement reporting requirements for mobility.
Radio link monitoring
  RAN4 is to identify the types of signals that are feasible for RLM requirements.