## Slide 1: Way forward capturing the proposals on further studies in RAN4 for NB-IOT
Ericsson
R4-160988
3GPP TSG RAN WG4 Meeting #78
Malta, 15-19 February, 2016
Agenda Item: 6.23.5

## Slide 2: Proposals on further studies NB-IoT
Radio link monitoring:
  Proposal #1: RLM performance of NB-IoT UEs is to be studied using following options, and the requirements can be defined accordingly.
    Option 1: Measurement based on secondary synchronization signal (P-SSS) is used for RLM for NB-IoT UE.
    Option 2: Measurement based on cell specific reference signals (e.g. CRS) and synchronization signals (e.g. P-SSS) are used for RLM by a NB-IoT UE.
Measurements:
  Proposal #1: RAN4 is to study RRM measurement performance using synchronization signal (NB-SSS) according to simulation assumptions in R4-160984
  Proposal #2: RAN4 is to study RRM measurement performance using both synchronization signals (NB-SSS) and CRS signals according to simulation assumptions in R4-160984.
System results:
  Minimum number of cells a NB-IOT device is required to detect is defined as:
Coverage mode: | # cells inband 10th percentile UE can detect (excluding serving cell): | # cells stand-alone 10th percentile UE can detect (excluding serving cell):
Basic mode | 5 | 5
Robust mode | 8 | 8
Extreme mode | 7 | 8