## Slide 1: Way Forward on IncMon alignment with legacy requirements
Nokia Networks, Alcatel-Lucent, Ericsson, TeliaSonera, China Telecom, Telecom Italia
R4-161055
3GPP TSG-RAN WG4 Meeting #78
St. Julian’s, Malta, 15th – 19th February, 2016
Agenda Item: 4.2.3

## Slide 2: Background
Since IncMon WI closure, alignment of the IncMon requirements with the legacy requirements for an FDD/TDD dual-mode UE has been discussed in RAN4 (e.g. [1, 2]).
In RAN4#77 it was proposed by a number of companies:
  IncMon UEs shall support legacy requirements in NPG as specified from Rel-8
  Align number of carriers in IncMon NPG for FDD/TDD dual mode UEs with legacy requirements for dual mode UEs from release 12
Alternative proposal was made during the meeting:
  IncMon UEs shall support legacy requirements in NPG as specified from Rel-8
  Align number of carriers in IncMon NPG for FDD/TDD dual mode UEs with legacy requirements for dual mode UEs from release 13
[1] R4-158027, Discussion on IncMon, Nokia Networks, Ericsson, DoCoMo, China Unicom, Alcatel Lucent, CMCC, Softbank, Telecom Italia, TeliaSonera, Verizon, China Telecom
[2] R4-158028, Regarding Inter-frequency FDD/TDD carriers in normal performance group in IncMon, Nokia Networks, Ericsson, DoCoMo, China Unicom, Alcatel Lucent, CMCC, Softbank, Telecom Italia, TeliaSonera, Verizon, China Telecom

## Slide 3: Background
Legacy UE requirement prior to introduction of IncMon:
  FDD/TDD dual mode UE shall be capable of monitoring at least 3FDD and 3TDD inter-frequency carriers.
Current IncMon UE requirement:
  FDD/TDD dual mode UE shall be capable of monitoring at least 8FDD and 8TDD inter-frequency carriers.
  Up to max 3 carriers (FDD and TDD) in NPG
  Rest in RPG
  If number of carriers in NPG exceeds 3 all configured carriers are treated equal (equally scaled).
Proposed IncMon UE requirement [2]:
  FDD/TDD dual mode UE shall be capable of monitoring at least 8FDD and 8TDD inter-frequency carriers.
  Up to max 3 FDD and 3TDD carriers in NPG
  Rest in RPG
  If number of FDD and TDD carriers in NPG exceeds 6 configured carriers are treated equal (equally scaled).

## Slide 4: Solution impact
IncMon is a mandatory feature.
Release 12 solution:
  Fluent alignment of requirements throughout the releases, no break in legacy behavior
  Aligned with legacy UE requirements and measurement capability
Release 13 solution
  Release 12 behavior will be ’special’ release behavior, special network handling of Release 12 IncMon UEs
  Different measurement capabilities and behavior among UEs in the field

## Slide 5: Way Forward
Due to identified complications of breaking legacy behavior for release 12 UE it is proposed:
  Align number of carriers in IncMon NPG for FDD/TDD dual mode UEs with legacy requirements for dual mode UEs from release 12
IncMon UE requirements from Rel-12:
  FDD/TDD dual mode UE shall be capable of monitoring at least 8FDD and 8TDD inter-frequency carriers.
  Up to max 3 FDD and 3TDD carriers in NPG
  Rest in RPG
  If number of FDD and TDD carriers in NPG exceeds 6 configured carriers are treated equal (equally scaled).