## Slide 1: 3GPP TSG-RAN WG4 Meeting #78 R4-161152 St. Julian’s, Malta, 15 - 19 February, 2016
WF for eMTC RF requirements
NTT Docomo, INC., Qualcomm, Huawei, Verizon, Ericsson, Intel, Sony

## Slide 2: Background
Several different methods for defining eMTC wayforward were discussed
Original proposal in RAN4#77 Anaheim was to reuse the 1.4 MHz emission requirements as such (R4-158447). This was not acceptable since it will lead to pessimistic MPR and A-MPR and requirements only for 1.4 MHz system BW were endorsed
Two methods are described in following pages

## Slide 3: Background Method 1
Keep transmission BW always 1.08 MHz and modify guardband depending on system BW
ACLR measurement BW is 1.08 MHz. In NTT Docomo proposal also SEM was considered similarly but only 1.4 MHz SEM was considered. This proposals would need more studies because e.g 20 MHz SEM is more stringent for the same offsets from the edge of the transmission BW. Than 1.4 MHz SEM.
Very carefull studies would be needed to understand which requirement is the most stringent for each new channel BW with the method proposed in these documents. In some cases even the inband emission requirement is the most sringent
Intel R4-77AH-IoT-0104
NTT Docomo R4-77AH-IoT-0058

## Slide 4: Background Method 2
Ericsson R4-77AH-IoT-0042
It is proposed that that Rel-13 LC/CE MTC UE should meet the emission requirements for different system bandwidths and the requirements for MPR should be set independently for each system bandwidth.
Qualcomm:
No new emission limits should be defined for eMTC UE but the testing should be done in multiple locations of the system BW.

## Slide 5: Way forward for eMTC emission requirements
  eMTC UE ability to meet all emission requirements (e.g. SEM, ACLR, spurious emission, in-band emission) will be checked for the next meeting
  For each system BW per band supported for eMTC:
    Study MPR against requirements as defined with respect to each system BW, for the edge RB position
    The guard band depends on the system BW
    Study A-MPR based on the outcome of MPR results
  No new emission table will be written for eMTC UE.
  Companies are encouraged to submit simulation results for the Power Class 3 and Power Class 5 UE in order to evaluate MPR and A-MPR