## Slide 1: 3GPP TSG-RAN WG4 Meeting #78 St. Julian’s, Malta, 15-19 February 2016
Huawei, HiSilicon, [Ericsson, Qualcomm, Intel, Samsung]
Way forward on demodulation performance and CSI requirements for LAA
R4-161182

## Slide 2: Test purposes for LAA demodulation
Verify the (e)PDCCH/PDSCH performance for bursty DL transmission that can be start at random subframe
Verify AGC/FTL/TTL tracking loop and CRS channel estimation performance with bursty CRS transmission.
  Verify the (e)PDCCH/PDSCH performance when the channels are in the initial partial subframe if UE support demodulation of initial partial subframe
    To verify UE have the right behavior for the start symbol detection (symbol 0 or symbol 7)
    To verify the new mapping for the second slot
Verify the (e)PDCCH/PDSCH performance when the channels are in the end partial subframe
  To verify the UE have the right UE behavior on the common PDCCH which indicates the number of symbols in the end partial subframe
Other test purposes are not precluded

## Slide 3: PDSCH demodulation requirements
        Introduce new PDSCH tests in CA mode with one licensed CC
Follow per-CC approach similar as that used for 3DL CA demodulation tests.
  Performance verification:
    Option 1: for LAA SCell only
    Option 2: for LAA Scell(s) and PCell
  The performance requirements are band agnostic and band combination agnostic.
        For PDSCH test, both CRS-based transmission scheme(s) and DMRS-based transmission scheme shall be covered

## Slide 4: PDSCH demodulation requirements test parameters
TM3 is used for licensed carriers
Transmission schemes of unlicensed carrier
  Option 1:
    TM3 for CRS-based transmission scheme
    TM9 for DMRS-based transmission scheme
  Option 2:
    TM3 and TM4 for CRS-based transmission scheme
      TM3 and TM4 for different antenna configuration
    TM9 for DMRS-based transmission scheme
  Other options are not precluded

## Slide 5: PDSCH demodulation requirements test parameters
Antenna configurations and correlation matrix:
  Option 1: 2x2 Low and 4x2 Low;
  Option 2: only 2x2 Low
  Other options are not precluded
Note: the antenna configuration for different test case may be different.
MBSFN subframe configuration
  Option 1:
    MBSFN subframe is not configured for CRS-based transmission mode
    MBSFN subframe is configured in subframes 1,2,3,4,6,7,8,9 for DMRS-based transmission mode
  Option 2
    MBSFN subframe is not configured for both CRS-based and DMRS-based transmission mode
DRS configuration
  The periodicity is FFS.

## Slide 6: PDSCH demodulation requirements test parameters
Propagation conditions:
  Option 1: EVA5 and/or EPA5
  Other options are not precluded
MCS: Starting point for further study
  Option 1: 16QAM 1/2 and 64QAM 1/2
  Other options are not precluded
Frequency offset and timing error, and synchronization:
  Frequency offset and timing error of LAA Scell should be set relative to Pcell
  Practical synchronization algorithm in UE should be considered;
  Other details are FFS
Reference receiver:
  MMSE-IRC receiver

## Slide 7: PDSCH demodulation requirements test parameters
Burst transmission model should be specified:
  Option 1: Explicitly model LBT transmission (Ericsson, R4-160367)
  Option 2: Design a repeated burst transmission pattern. pre-define 8 types of burst pattern, after the previous burst transmission, randomly decide to chose which burst type out of 8 types (Huawei, R4-160742)
  Option 3: Define DL burst transmission model based on Poisson arrival process. Number of subframes in a transmission burst is chosen uniformly from {4,5,6,7,8}. (QC, R4-160046)
  More input from other companies are highly welcome.
RAN1 decision on LAA UE capability related to reception on initial partial subframe should be taken into account when specifying the requirements

## Slide 8: PDSCH demodulation requirements test parameters
Test metric
  Option 1: Reusing relative throughput
    Considering updating the relative throughput definition as given in R4-160368
    70% TP as starting point.
  Other options not precluded

## Slide 9: Control channel demodulation requirements
        PDCCH and EPDCCH performance verification:
  Option 1: Specify the PDCCH and EPDCCH performance requirements
    The details parameters are FFS
    Test metric:
      Using BLER metric as starting point
  Option 2: Implicitly verify the PDCCH and EPDCCH performance via PDSCH tests

## Slide 10: Test purpose for LAA CSI
The following test purposes can be considered for the LAA CSI test:
  UE should not average CRS/CSI-RS measurements across transmission bursts.
  UE should find the right CSI reference resource in FS3
  Other purposes are not precluded

## Slide 11: CSI test
At least one CSI test for CRS based transmission scheme and at least one CSI test for DMRS based transmission scheme
  For other CSI test case, it is FFS
CQI feedback mode
  Option 1: Introduce the aperiodic CQI test
  Option 2: Introduce the periodic CQI test
Transmission mode
  Option 1: consider TM3 and TM9
  Option 2: consider TM2 and TM9
  Other options are not precluded
Test methodology
  Companies are encouraged to bring in proposals for CQI test methodology in next meeting.