## Slide 1: 3GPP TSG-RAN WG4 Meeting #78 St. Julian’s, Malta, 15-19 February 2016
Huawei, HiSilicon, Ericsson,Nokia Networks, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell
Way forward on eMTC BS demodulation performance requirements
R4-161215

## Slide 2: BS demodulation requirements
        Define BS PRACH/PUCCH/PUSCH demodulation requirements
  Option 1: Define one set of requirements, i.e. not separating requirements with respect to CE Mode A and CE Mode B
            one set of requirements to cover both FDD and TDD.
  Other options are not precluded
        Study and decide the combination of MCS and repetition level for BS demodulation performance requirements

## Slide 3: BS demodulation requirements - Test cases
        PRACH
        Define the Cat-M PRACH performance requirements in terms of the probabilities of [0.1%] false alarm and [99%] detection probability as the requirement for regular UEs
        Define Performance for preamble format 0 ~ format 3 except format 4 with repetition and frequency hopping
        No need to have Cat-M PRACH performance requirements for high speed mode
        PUCCH
        Define a uniform set of requirements to cover both FDD and TDD
        Introduce PUCCH demodulation requirements for format 1a and format 2 with repetition and frequency hopping
        PUSCH
        Define one set of requirements to cover both FDD and TDD
        Introduce PUSCH demodulation requirement with repetition and frequency hopping
        Simulation parameters
        The detailed simulation parameters are given in R4-161227, R4-161228 and R4-R4-161217