## Slide 1: Way forward on BS receiver requirements for NB-IoT
Huawei, Ericsson, NTT DOCOMO, …
3GPP TSG-RAN WG4 Meeting #78 R4-161275
Malta, 15-19 Feb, 2016

## Slide 2: Reference
[1] R4-160179, “BS Rx RF requirement for NB-IoT(in-band/guard-band)”, NTT DOCOMO INC.
[2] R4-160613, “On BS REFSENS for NB-IoT”, Huawei
[3] R4-160914, “BS RF: REFSENS requirement”, Ericsson
[4] R4-160910, “Way forward on BS RF requirements”, Ericsson

## Slide 3: Background
This contribution captures the intial consensus for NB-IoT BS receiver requirements.

## Slide 4: Receiver requirements
BS REFSENS
  Methodology
    Reference sensitivity level is the minimum mean received signal strength to meet 95%of the maximum throughput. REFSENS can be calculated as follows:
    REFSENS = -174+10*log10(BW) + NF + IM + SNR
    Where:
      BW is the transmission bandwidth in Hz,
      NF is the receiver noise figure in dB,
      IM is implementation margin in dB,
      SNR in dB to meet the 95% of maximum throughput under fixed reference channel (FRC)
    For wide area base station, NF = 5, IM = 2.

## Slide 5: Receiver requirements
BS REFSENS (cont.)
  Operation mode
    Single same requirement specified for all 3 operation modes
  Requirements
    Option1: Specify requirement for single-tone transmission of both 3.75kHz and 15kHz.
    Option2: Sepcify requirement for single-tone transmission of both 3.75kHz and 15kHz, as well as 3 tones of multi-tone transmission. The requirement for 3 tones transmission could be applied for each 3 tones of 6 and 12 tones for multi-tone transmission.

## Slide 6: Receiver requirements
BS REFSENS (cont.)
  Configration of FRC for both options
    3.75kHz and 15kHz for single-tone
    3 tones transmission for multi-tone (if option 2 is selected)
    Pi/2-BPSK for single-tone
    QPSK for multi-tone (if opition 2 is selected)
    Repetition is not considered
    Others (including transport block size, coding rate, etc.) are FFS.

## Slide 7: Receiver requirements
Others need to be investigated
  Dynamic range
  In-band selectivity
  ACS and narrowband blocking
  Blocking
  Receiver intermodulation
Note: [1] can be used as a reference for initial discussion for other requirements.